## Slide 1: Building A Quadcopter in 10 Weeks
To achieve great things, two things are needed: a plan and not quite enough time.
--Leonard Bernstein
Homepage: http://goo.gl/XYwuoy

## Slide 2: Course Goals
Build several small quadcopter
  In 10 weeks
  Mostly “from scratch”
Learn
  Basic PCB design
  How to integrate diverse hardware/software components
  About quadcopter-related technologies

## Slide 3: Course Schedule Outline
Main goal: Start testing/refining flight control software on your quad ASAP.
Weeks 1-5: Sprint to a PCB design, do preliminary software development
  Most important date: May 9th – Board “tape out”
Weeks 6-10: Software refinement, quad assembly, refinement and testing.
Schedule is here: https://goo.gl/LgzvEu

## Slide 4: Lab Overviews

## Slide 5: The Lab Schedule
The lab schedule is very aggressive
Preparatory labs (1-4): 2 weeks
  There’s a new lab each class, and they are due one week later.
  You will learn all the skills you need to build the quadcopter
Design and manufacturing labs (4,7,8): 3.5 weeks
  Design the schematic and board
  Manufacture them.
Implement flight control software (5, 6): 4 weeks
  Quadcopter and remote firmware development
  PID control for quad stability.
Make it work labs (9-10): 4.5 weeks
  Make it fly!
Total: 14 weeks!
Do not fall behind!

## Slide 6: Lab Structure
Labs are divided into hardware and software labs
Hardware labs require equipment
  We will provide it.
  You are responsible for it (see policy on course web site)
Software labs require only software and data

## Slide 7: Teams
You will work both in groups and on your own
Lab 1 and 2 will be on your own.
Labs 3 will completed in pairs of my choosing.
The rest are completed in pairs of your choosing.
In all cases, you can help each other out
  No direct copying of source code, designs, etc.
  Asking questions, etc. is great.
  There is no curve in this class – no need to compete.

## Slide 8: Lab 1: Learn to Use Eagle
Software Lab
Build design a simple schematic.
Turn it into a board design.
Generate manufacturing data.
Performance manufacturing checks.
Design some new parts for the Eagle library.
Learn to decorate your boards.
This is due Thursday (in 48 hours!!!)

## Slide 9: Lab 2: Practice Using Eagle
Software Lab
Build more parts in Eagle.
  The IMU
  Some discrete components
Hard: Build all the parts.

## Slide 10: Lab 3: Wireless Communication
Hardware Lab
Learn how to use the microcontrollers
  Arduino IDE
  The microcontroller breakout boards
  The radios
Experiments
  Measure bandwidth, error rate, and range

## Slide 11: Lab 4: Start Designing the Quad
Software Lab
Create the schematic
  Start with the breakout board schematic.
  Connect the IMU
  Connect the motor controller
  Assemble the power supply circuit
Followed by design review

## Slide 12: Lab 5: Other Quadcopter Components
Hardware Lab
Use the remote control to measure gimbal position
Transmit it to the other red board and control a motor accordingly
Read values from an IMU.
Hard: Write some flight control “utilities”

## Slide 13: Lab 6: Flight Control Software
Hardware Lab
Implement PID control
Build a remote-controlled, PID stabilized test stand.

## Slide 14: Lab 7: Layout the Board
Software Lab
Define the board outline.
Place your parts.
Route the design.
Followed by design review.
Design review

## Slide 15: Lab 8: Tape Out!!!
Software Lab
Your designs must be ready for manufacturing by the beginning of class on May 11th.
Early tape out is possible on May 4th.
It will take about a week to manufacture them.

## Slide 16: Lab 9: Assembly and Bringup
Hardware Lab
Solder everything to the board
  This is non-trivial. The Microcontroller and IMU are challenging packages.
Install the bootloader
Test all the quad subsystems
  IMU
  Motors
  Power
  Radio
Debug, Debug, Debug.

## Slide 17: Lab 10: Make it Fly!!!
Software and Hardware Lab
Test, adjust, tweak, debug, etc. until its flight is stable.

## Slide 18: Logistics

## Slide 19: Lab Materials
We will distribute lab materials via github classroom.
You’ll need a github account.
You’ll need to know how to use git.
To access the lab materials, click on the invitation link included in each lab.

## Slide 20: Grades and Stuff
No final or exams.
10 Labs
Grading breakdown
  50% class participation
  50% labs

## Slide 21: This is an Intensive, Hands-on Class
Not so much lecturing
Lots of doing.
Your Task
  Work Hard
  Figure stuff out
  Take the initiative
My and Antonella’s Task
  Provide high-level guidance
  A few lectures
  Make sure you have what you need to succeed.

## Slide 22: Lab Space
We will meet and work in this room (EnVision -- SME)
Class: 11-12:30
Lab hours
  12:30on Tuesday and Thursday
  Other times TBD

## Slide 23: Lab 3: Arduino and Wireless

## Slide 24: The “Red Board”
Nice breakout board for our microcontroller
  Open source
  Working radio design
  Well-documented
Arduino compatible
  Programmable with FTDI USB-to-serial converter
Key component of the controller
Reference design for the quadcopter’s flight computer and radio.

## Slide 25: The Arduino IDE
User-friendly IDE for Arduino programming
  Programming the microntroller is easy
  Installation is easy
Alternatives
  Eclipse for Arduino
  Official AVR tools from Atmel
  You can use them, but they aren’t supported by us.

## Slide 26: Tasks
Get wireless working
  Download, compile, and install a simple chat program that runs between two red boards.
Push its limits
  Do some simple experiments to
  Measure range, bandwidth, and the error rate

## Slide 27: Quadcopters

## Slide 29: Multirotor Aircraft Components
Airframe
  Structural support
  Plastic, aluminum, wood, or PCB (fiberglass)
Motors
  Lift, movement, and control
  Brushed DC motors for small craft
  Brushless brushless DC motors for large craft.
Inertial Measurement Unit (IMU)
  Sensing the aircraft’s orientation and movement
  Gyroscopes and accelerometers.
Computing resources (microcontroller/processor)
  To run the flight control software
  Manage communication
Flight control software
  Provides stability using the IMU and motors
  Converts pilot commands to motor outputs
Radio
  For receiving command
  Returning telemetry.
Power supply
  Lots of power for the motors
  Carefully regulated power for the IMU and micro controller.

## Slide 30: Principles of Operation (1)
Z
Y
X
An even number of motors provides lift and control in 6 dimensions
  Spatial dimensions: x, y, z
  Pitch: rotation around left-right (y) axis
  Roll: rotation around the front-back (x) axis
  Yaw: rotation around the top-bottom (z) axis
A flight computer operates a closed-loop controller to maintain stability and implement pilot commands.

## Slide 31: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 32: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 33: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 34: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 35: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 36: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 37: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 38: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 39: Inertial Measurement Unit
STMicro LSM9DS0
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
I2C interface (more on this later)

## Slide 40: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7V
  Powers the motors directly
3.0V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU
  Why 2.7 or 3V instead of 3.3V?

## Slide 41: Motors and Props
Suitable motors are hard to find in small quantities.
Correct-fitting props are also a challenge
We will use motors for the Hubsan X4
  Purchased as a “crash pack”
  Plenty of power
  DC brushed motors
  They draw ~2A each.

## Slide 42: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it’s off.

## Slide 43: Wireless Communication
We will use a custom (i.e., designed by you) communication protocol between the controller an the quadcopter.
Why not one of the existing alternatives?
  Standard RC radio protocols are analog or closed source.
  Zigbee is complex and closed source.

## Slide 44: Flight Control Software (Option 1)
Use the MultiWii flight controller software
  Open source
  Arduino-compatible
  Widely used
  A GUI
  (but not with out it’s idiosyncracies)
You’ll implement the PID controller.

## Slide 45: Flight Control Software (Option 2)
Write it from scratch
  We will still use the GUI

## Slide 46: Controller
The controller sends commands to the quadcopter via the radio.
We have a controller design ready for you
  It uses the same microcontroller we are using
  You’ll be able to customize it a bit.

## Slide 47: What You Will Build

## Slide 48: What You Will Build