## Slide 1: Quadcopters

## Slide 3: Multirotor Aircraft Components
Airframe
  Structural support
  Plastic, aluminum, wood, or PCB (fiberglass)
Motors
  Lift, movement, and control
  Brushed DC motors for small craft
  Brushless brushless DC motors for large craft.
Inertial Measurement Unit (IMU)
  Sensing the aircraft’s orientation and movement
  Gyroscopes and accelerometers.
Computing resources (microcontroller/processor)
  To run the flight control software
  Manage communication
Flight control software
  Provides stability using the IMU and motors
  Converts pilot commands to motor outputs
Radio
  For receiving command
  Returning telemetry.
Power supply
  Lots of power for the motors
  Carefully regulated power for the IMU and micro controller.

## Slide 4: Principles of Operation (1)
Z
Y
X
An even number of motors provides lift and control in 6 dimensions
  Spatial dimensions: x, y, z
  Pitch: rotation around left-right (y) axis
  Roll: rotation around the front-back (x) axis
  Yaw: rotation around the top-bottom (z) axis
A flight computer operates a closed-loop controller to maintain stability and implement pilot commands.

## Slide 5: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 6: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 7: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 8: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 9: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 10: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 11: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 12: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 13: Inertial Measurement Unit
STMicro LSM9DS0
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
I2C interface (more on this later)

## Slide 14: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7V
  Powers the motors directly
3.0V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU
  Why 2.7 or 3V instead of 3.3V?

## Slide 15: Motors and Props
Suitable motors are hard to find in small quantities.
Correct-fitting props are also a challenge
We will use motors for the Hubsan X4
  Purchased as a “crash pack”
  Plenty of power
  DC brushed motors
  They draw ~2A each.

## Slide 16: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it’s off.

## Slide 17: Wireless Communication
We will use a custom (i.e., designed by you) communication protocol between the controller an the quadcopter.
Why not one of the existing alternatives?
  Standard RC radio protocols are analog or closed source.
  Zigbee is complex and closed source.

## Slide 18: Controller
The controller sends commands to the quadcopter via the radio.
We have a controller design ready for you
  It uses the same microcontroller we are using
  You’ll be able to customize it a bit.

## Slide 19: The Hardware You will Build

## Slide 20: The Hardware You Will Build

## Slide 21: The Software You will Build
Firmware for the remote
  Measure inputs
  Transmit them.
Flight control software for the quadcopter
  Sense orientation
  Maintain level flight
  Respond to RC commands.

## Slide 22: Lab 3: Make all Your Hardware Work a.k.a Remote Controlled Motors

## Slide 23: Tasks
Meet the hardware
Get Arduino working
Read from the gimbals
Communicate with a radio
Assemble your test stand
  Build 4 motor drivers
  Wire everything up
Control your motors via the remote control.

## Slide 24: The “Red Board”
Nice breakout board for our microcontroller
  Open source
  Working radio design
  Well-documented
Arduino compatible
  Programmable with FTDI USB-to-serial converter
Key component of the controller
Reference design for the quadcopter’s flight computer and radio.

## Slide 25: The Test Stand

## Slide 26: The Arduino IDE
User-friendly IDE for Arduino programming
  Programming the microntroller is easy
  Installation is easy
Alternatives
  Eclipse for Arduino
  Official AVR tools from Atmel
  You can use them, but they aren’t supported by us.

## Slide 27: The Inputs and Outputs
Gimbals – How they work and how to read them.
Brushed Motors – How they work and how to drive them.
The IMU – microcontroller and IMU communicate.
The serial display, LEDs, etc. – Communicating with the pilot.

## Slide 28: Gimbals

## Slide 29: Controlling the Quadcopter
Standard RC “transmitters” have two sticks
  Left: throttle and yaw
  Right: pitch and roll
  This is called “mode 2” It’s different in Europe where they use “mode 1”
Yaw, pitch, and roll are spring-loaded to return to neutral
Throttle stays where you put it.

## Slide 30: The Gimbals
Each stick is a “gimbal”
  a mechanism, typically consisting of rings pivoted at right angles– The dictionary on my Mac

## Slide 31: Anatomy of a Gimbal
Two potentiometers measure X and Y movement of the stick.
Potentiometer – A variable voltage divider
  As the slider’s movement changes the resistance from A and W and W and B.
  The voltage at W is proportional to the position of the gimbal.
In reality, the resistances are always > 0, so W never reaches VCC or GND.
Our gimbal
  Frsky PR10
  Total resistance: 2.4KOhms
  Rated voltage: 5V

## Slide 32: Reading the Gimbals
The red board board has several analog input pins
analogRead(int pin)
  Takes a voltage between GND and Vcc and maps it to 0—1024
Check the schematic for the remote to see which pins are attached to which gimbals
    https://github.com/NVSL/Quadcopter-Remote

## Slide 33: Brushed DC Motors

## Slide 34: Brushed Motors

## Slide 35: Construction

## Slide 36: Construction (Rotor)

## Slide 37: Construction (Stator)

## Slide 38: Operation

## Slide 39: Operation

## Slide 40: Operation

## Slide 41: Operation

## Slide 42: Operation

## Slide 43: Flyback
Opening S1 makes M1 an inductor
  Drives up voltage M1-
  Can destroy the switch
  Can cause current to back to power supply.
  Causes noise on power supply.
This is called “fly back”
Adding a diode relieves the problem.

## Slide 44: Control
How would you control your motor’s speed?
  Speed ∝Voltage ∝Current
So, vary the input voltage
Generating varying voltages is non-trivial
  You need an digital-to-analog converter
Really, we just need the average voltage to vary

## Slide 45: Pulse-width Modulation (PWM)

## Slide 46: Selection
Free Speed:100 rpm
Stall Torque:8.6 in-lbs
Stall Current:2.6A
Free Current:0.18A
Specifications at 7.2V

## Slide 47: Our Motor Circuits

## Slide 48: PWM in Arduino
The red board board has several analog output (PWM) pins
analogWrite (int pin)
  Takes a value, x, between 0 (off) and 255 (on) and sets the duty cycle to x/255.

## Slide 49: The Serial LCD Display

## Slide 50: Display Text on the Remote
The LCD display on the remote is connected to the second serial port on the redboard
The LCD_library provides a nice interface for writing to it
  Docs here: http://playground.arduino.cc/Code/SerLCD

## Slide 51: Other Components

## Slide 52: Status LEDs
The remote has 3 status LEDs (D3, D4, D5) in the upper left of the control board.
They are useful for letting you know when the quad is armed, etc.
Use digital_write() to control them.

## Slide 53: Buttons
The remote has 2 buttons (B1, B2) for your use.
Use digital_read() to see if they are pressed.

## Slide 54: Pots
The remote has 2 potentiometers (TM1, TM2)
Use analog_read() to get their value.

## Slide 55: Lab Tasks
Use everything
  Install IMU library. Read values from IMU.
  Read the values from the gimbals.
  Display things on the serial display.
  Drive a motor.
  Turn the indicators on and off.
  Read values from the pots.
  Use the buttons to do something
Build a remote-controlled motor
  Stand alone red board drives motor.
  Remote control reads gimbals and transmits value to run motor at.
  This is the basic frame work for your quadcopter and remote firmware.