## Slide 1: Lab 4a: Schematic Assembly

## Slide 2: Groups
You must form your groups by 2pm today.

## Slide 3: What You Will Build

## Slide 4: What You Will Build

## Slide 5: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7V
  Powers the motors directly
3.0V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU
  Why 2.7 or 3V instead of 3.3V?

## Slide 6: Regulator Datasheet

## Slide 7: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 8: uController Datasheet

## Slide 9: Wireless Communication
We will use a custom (i.e., designed by you) communication protocol between the controller an the quadcopter.
Why not one of the existing alternatives?
  Standard RC radio protocols are analog or closed source.
  Zigbee is complex and closed source.

## Slide 10: Motors and Props
Suitable motors are hard to find in small quantities.
Correct-fitting props are also a challenge
We will use motors for the Hubsan X4
  Purchased as a “crash pack”
  Plenty of power
  DC brushed motors
  They draw ~2A each.

## Slide 11: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it’s off.

## Slide 12: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
We will use the I2C interface

## Slide 13: IMU datasheet
Notes
  You can tie all the RES/GND pads to one pin on the schematic symbol

## Slide 14: Inter-Integrated Circuit (I2C) Bus Interface AKA: Two Wire Interface (TWI)

## Slide 15: Brief History
Designed in 1982 by Philips Semiconductor (now NXP)
1992 - First public Spec released
Since 2006 no licensing fees are required
Widely adopted technology

## Slide 16: Why I2C?
Pins are precious!
  They take up space
  More pins  More expensive microcontrollers
  Adding pins is hard
    Might need a new microcontroller (if a larger, compatible one is available)
    Significant board changes
Performance is often not that important
So
  Use the minimum number of pins
  Run them at relatively low bit rates.

## Slide 17: Applications
Connecting to all kinds of small, slow peripherals
  Reading Configuration data from various devices (Memory, PCI cards)
  Accessing ADCs and DACs
  Reading from Real-time clocks
  Reading hardware monitoring devices (Fan speed, CPU Temperature, Accelerometers)
  Controlling power supplies for various system components
  GPIO expanders
  Many, many others

## Slide 18: I2C Bus Architecture
Two signals
  SCL – Serial Clock (used for coordination and timing)
  SDA – Serial Data (used for data and control signaling)
Up to 1008 peripherals
  1 or more “masters” that initiate communication on the bus
  Up to 127 “slaves” that masters communicate
Bit rates
  100 KHz (Standard mode)
  400 KHz (Fast Mode)
  3.4 MHz (High speed mode)
  1 MHz (Fast Mode Plus)
  5 MHz (Ultra fast mode)

## Slide 19: I2C Addressing
Each slave on an I2C bus has a unique address.
  Most use 7 bit addresses (we discuss this here)
  An extended 10-bit version also exists
The addresses usually fixed or only partially configurable
  E.g. Only the least-significant bit of the address for the IMU is settable. So you can only have two of these IMUs on one bus.
  Different devices will have different numbers of settable and fixed bits.
  You can’t mix components arbitrarily on the bus

## Slide 20: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Start

## Slide 21: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Address
R/W

## Slide 22: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Data

## Slide 23: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Stop

## Slide 24: Breakout header

## Slide 25: Custom LEDs

## Slide 26: Lab4b: Design Review
Once your design is complete, you are ready for your first design peer review.
Your schematic should have no errors or warnings.