## Slide 1: Lab 4a: Schematic Assembly

## Slide 2: What You Will Build

## Slide 3: What You Will Build

## Slide 4: Three Schematic Design Skills
Copy – You will manually copy the microcontroller circuit from the remote.
Copy – you’ll copy the motor controller based on a schematic I provide.
Implement – You will look at the data sheet for the IMU and voltage regulator and implement the design it provides.
Design – you will add some LEDs to your design on your own.

## Slide 5: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7V
  Powers the motors directly
3.3V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU

## Slide 6: Regulator Datasheet

## Slide 7: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 8: uController Datasheet

## Slide 9: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
We will use the I2C interface

## Slide 10: IMU datasheet
Notes
  You can tie all the RES/GND pads to one pin on the schematic symbol

## Slide 11: Motors and Props
Plenty of power
DC brushed motors
They draw ~2A each.

## Slide 12: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it’s off.