## Slide 1: Today After Lecture
Find Harshini or I to demo Lab 3

## Slide 2: Lab 6: Sensing and Control

## Slide 4: Principles of Operation (1)
Z
Y
X
An even number of motors provides lift and control in 6 dimensions
  Spatial dimensions: x, y, z
  Pitch: rotation around left-right (y) axis
  Roll: rotation around the front-back (x) axis
  Yaw: rotation around the top-bottom (z) axis
A flight computer operates a closed-loop controller to maintain stability and implement pilot commands.

## Slide 5: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 6: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 7: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 8: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 9: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 10: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 11: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 12: Step 1: Find Your Orientation
Lab 6a

## Slide 13: Lab 6a: Tasks
Install IMU library. Read values from IMU.
Use Arduino’s plotting tool
Run your serial port at max speed!!! (If you can)
Write software to cleanly read the attitude of the pivot platform while the motors are running.

## Slide 14: Demo
Look at AHRS code
Demo Euler angle measurements and noise
Demo complimentary filter
Look at code for setting parameters over I2C
Look at IMU datasheet section about register settings.

## Slide 15: Quadcopter Software

## Slide 16: Remote Software Path
Scale gimbal readings (-512-512 for P,R, Y; 0-1023 for T)
“deadband” avoids noise near the mid point.
Performance is not critical 10-20Hz updates is more than enough.

## Slide 17: Quadcopter Datapath
Slow: Translate gimbal reads into ‘set points’
Fast: Use PID to track set points.

## Slide 18: The PID Controller

## Slide 19: To add
Discuss different ways they can control their quad
  Pitch/roll -> rate of change of angle
  Pitch/roll -> angle of attack
  Pitch/roll -> velocity
  Pitch/roll -> position
  Throttle -> throttle
  Throttle -> rate of climb
  Throttle -> altitude
Discuss higher-order control
  How to integrate GPS
  How to integrate barometer

## Slide 20: Note for Next Class
Demo
  Integral windup
  Tuning PID
Combine this lecture with the flight control software lecture

## Slide 21: Control Theory
Making a physical system do what you want
“Open loop” and “closed loop”
Open loop - cannot see the system’s output
  Motor controllers
  LCD/LED/CRT screens
Closed loop - Can see output, make corrections
  Autopilot
  GPS guided munitions
  Our quadcopter

## Slide 22: What is PID?
Make a system follow a set point
“Proportional, Integral, Derivative”
A brief history:
  1788 - James Watt’s flyball governor (P)
  1837 - Louis Molinié hydraulic regulator (PI)
  1857 - H.N. Throop marine engine governor (PD)
  1868 - Maxwell gives theoretical basis
  1911 - Elmer Sperry, ship steering (PID)

## Slide 23: Closed loop control
PID is the most common closed loop controller
Proportional: Directly against error
Integral: Remembers error over time
Derivative: Dampens response to avoid oscillations

## Slide 24: Example
https://sites.google.com/site/fpgaandco/pid

## Slide 25: PID on the Quadcopter
3 separate controllers
PID set point is from user

## Slide 26: Pitfalls of PID
Integral term “Windup”
  One solution: Exponential decay on integral (E.g., I = I/2 + error)
Derivative noise: beware of noise.
Error term with vibration
Derivative term causes your system to go insane
  Solution: moving average of last several values. Or median of last several values.
  Using the serial plotter in arduino to watch the D term.
3. Tweaking PID values
Tune P first, then D, then I.

## Slide 27: Implementation
NOTES:
  Where to get the derivative?
  Integral windup
  Pay attention to rate (hz)
  Relative scale of inputs and outputs
    Make sure timestep is consistent

## Slide 28: How important in speed?
The key number is how many times/sec your PID loops (Hz)
The internet suggests > 100Hz (10ms/cycle) is necessary for stable flight.
My non-optimized code runs at 400Hz (2.5ms/cycles)
Action | Latency (ms)
Reading IMU | 7.360
analogWrite() | 0.012
analogRead() | 0.104
Integer PID (one channel) | 1.880 (531Hz)
FP PID (one channel) | 1.888 (529Hz)
AHRS getOrientation() | 1.860
rfWrite() 16 bytes | 0.812
Serial.write(“a”) | 0.906

## Slide 29: Tuning
Tuning PID is a bit of an art form.
Simple algorithm
  Set P=I=D = 0
  Increase P until it starts oscillating, reduce until it oscillates just a bit
  Increase D to till it stabilizes pretty quickly
  Increase I to fix offset
  Increase D as much as possible with causing oscillation.

## Slide 30: Tuning
Zeigler-Nichols method.
  P=I=D= 0
  Increase P until oscillations start. P is now at Ku, oscillation is at frequency Tu.
  Follow the chart.
  It’s important that your PID look incorporate its execution interval correctly.