## Slide 1: Project Overview
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 3: Multirotor Aircraft Components
Airframe
  Structural support
  Plastic, aluminum, wood, or PCB (fiberglass)
Motors
  Lift, movement, and control
  Brushed DC motors for small craft
  Brushless brushless DC motors for large craft.
Inertial Measurement Unit (IMU)
  Sensing the aircraft’s orientation and movement
  Gyroscopes and accelerometers.

## Slide 4: Multirotor Aircraft Components
Computing resources (microcontroller/processor)
  To run the flight control software
  Manage communication
Flight control software
  Provides stability using the IMU and motors
  Converts pilot commands to motor outputs
Radio
  For receiving command
  Returning telemetry.
Power supply
  Lots of power for the motors
  Carefully regulated power for the IMU and micro controller.

## Slide 5: Principle Axes of an Aircraft
Pitch – leaning front or back
Roll -- leaning side to side
Yaw – rotating

## Slide 6: Motor Configurations
“multirotor” is more accurate that “quadcopter”
There are always an even number of motors
  Half spin clockwise
  Half spin counter-clockwise

## Slide 7: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
  Quad moves forward
Pitch backward
  Less thrust to the rear
  More to the back
  Quad moves backward
Net torque is constant

## Slide 8: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
  Quad moves to the left
Pitch Right
  More thrust to the left motor
  Less to the Right
  Quad moves to the right
Net torque is constant

## Slide 9: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW
Net thrust is constant

## Slide 10: Quadcopters (and the Environment) are Imperfect
Motors are not perfect
  Manufacturing differences
  Electrical differences
  Propeller imperfections
Air currents will move the quadcopter.
Turning on all motors the “same” amount
  Leads to imbalanced torque and uneven thrust.
  A crash is inevitable
  This is “open loop” control

## Slide 11: Closing the Loop for Controlled, Stable Flight
Quadcopters sense the orientation
  IMU – Inertial Measurement Unit
  Measures pitch, roll, and yaw
The flight computer, adjusts motor outputs to achieve a target orientation
  Level – stationary flight
  Pitched forward – fly forward
  etc.
The target can be set via a remote to control flight.

## Slide 12: Open vs. Closed Loop Control

## Slide 13: In Summary: Flight Requirements and Our Labs
Requirement | Hardware | Software | Manufacturing
Driving the motors | Motors, battery, airframe, etc. Building The Quadcopter Schematic Laying Out The Board | Analog pin output Programming The Hardware | 
Providing a target orientation (via the remote) | A radio, a remote control Building The Quadcopter Schematic Laying Out The Board | Communication protocol Programming The Hardware | 
Sensing the quadcopter’s orientation | An IMU Building The Quadcopter Schematic Laying Out The Board | Filter out noise, a little math Sensing and Filtering | 
Adjusting motor output to achieve the target orientation |  | A clever control algorithm Implementing PID | 
Stable flight |  | A lot of tuning Flight | 
Assembled quadcopter |  |  | Tape-out, Assembly, and Bring-up PCB Assembly

## Slide 14: Our Project
Motors
IMU
Flight control software
Radio

## Slide 15: The Hardware You will Build

## Slide 16: The Hardware You Will Build

## Slide 17: Flight Computer: ATmega128RFA1 microcontroller
Arduino compatible
16Mhz clock
128KB Flash
16KB SRAM
4096B EEPROM
2.4GHz radio

## Slide 18: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
I2C interface

## Slide 19: Power Supply
Lithium Polymer Battery
  370-600 mAh
  Max Current: 9.25 Amps (a lot!)
  Nominal voltage: 3.7-4.2V
  Powers the motors directly
3.3V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU

## Slide 20: Motors and Props
DC brushed motors
Max current: ~2 Amps
Plenty of power