## Slide 1: Quadcopters

## Slide 3: Multirotor Aircraft Components
Airframe
  Structural support
  Plastic, aluminum, wood, or PCB (fiberglass)
Motors
  Lift, movement, and control
  Brushed DC motors for small craft
  Brushless brushless DC motors for large craft.
Inertial Measurement Unit (IMU)
  Sensing the aircraft’s orientation and movement
  Gyroscopes and accelerometers.
Computing resources (microcontroller/processor)
  To run the flight control software
  Manage communication
Flight control software
  Provides stability using the IMU and motors
  Converts pilot commands to motor outputs
Radio
  For receiving command
  Returning telemetry.
Power supply
  Lots of power for the motors
  Carefully regulated power for the IMU and micro controller.

## Slide 4: Principles of Operation (1)
Z
Y
X
An even number of motors provides lift and control in 6 dimensions
  Spatial dimensions: x, y, z
  Pitch: rotation around left-right (y) axis
  Roll: rotation around the front-back (x) axis
  Yaw: rotation around the top-bottom (z) axis
A flight computer operates a closed-loop controller to maintain stability and implement pilot commands.

## Slide 5: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 6: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 7: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 8: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 9: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 10: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 11: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 12: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 13: Inertial Measurement Unit
STMicro LSM9DS0
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
I2C interface (more on this later)

## Slide 14: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7V
  Powers the motors directly
3.0V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU
  Why 2.7 or 3V instead of 3.3V?

## Slide 15: Motors and Props
Suitable motors are hard to find in small quantities.
Correct-fitting props are also a challenge
We will use motors for the Hubsan X4
  Purchased as a “crash pack”
  Plenty of power
  DC brushed motors
  They draw ~2A each.

## Slide 16: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it’s off.

## Slide 17: Wireless Communication
We will use a custom (i.e., designed by you) communication protocol between the controller an the quadcopter.
Why not one of the existing alternatives?
  Standard RC radio protocols are analog or closed source.
  Zigbee is complex and closed source.

## Slide 18: Flight Control Software (Option 1)
Use the MultiWii flight controller software
  Open source
  Arduino-compatible
  Widely used
  A GUI
  (but not with out it’s idiosyncracies)
You’ll implement the PID controller.

## Slide 19: Flight Control Software (Option 2)
Write it from scratch
  We will still use the GUI

## Slide 20: Controller
The controller sends commands to the quadcopter via the radio.
We have a controller design ready for you
  It uses the same microcontroller we are using
  You’ll be able to customize it a bit.

## Slide 21: What You Will Build

## Slide 22: What You Will Build