## Slide 1: PCB Assembly

## Slide 2: The PCB Assembly Process
Apply solder paste with a stencil
  https://learn.adafruit.com/smt-manufacturing/squeegees
Place parts
Reflow in an oven
Solder on through-hole components.

## Slide 3: Align Stencil
Good
Bad

## Slide 4: Solder Squeegees

## Slide 5: Our “squeegee”
Photos: Adafruit.com

## Slide 6: Applying Solder Paste
Good
Bad

## Slide 7: Part Placement
Good
Good

## Slide 8: Reflow Soldering

## Slide 9: Reflow Video

## Slide 10: Reflow Soldering Results
Good
Bad

## Slide 11: Solder Joints

## Slide 12: Process For the Lab: Collect parts, apply paste
Collect parts
  Grab 1 packet of each type of part.
  They are laid out in the lab.
  Do not open them until you are ready to place them.
Apply paste
  Read lab write up carefully.
  Wear gloves
  Check stencil alignment
  Put paste on squeegee
  Apply!
Check it yourself
Get it checked by staff

## Slide 13: Process For the Lab: Place parts
Place parts in order given in lab write up.
  Some parts are not used on the BBB.
Open packets of parts one at a time
Tips
  Double check values (e.g., “1uF”) to ensure proper placement
  Double check orientation on diodes, LEDs, the micro controller, and the balun.
  Don’t fiddle.

## Slide 14: Process For the Lab: Reflow and Touch Up
Course staff will run boards through the reflow oven in batches
Check boards for solder bridges and other problems.
If touch up is necessary, staff will guide.

## Slide 15: Process For the Lab: Throughhole Parts
There are a few throughhole parts
  Headers
  Power terminals
Tape them in place with blue tape
Staff will demo throughhole soldering.

## Slide 16: Process For the Lab: Bring Up
First, check for shorts between power and ground
Flash bootloader
  Borrow the ISP programmer.
  Follow lab instructions to flash the bootloader.
Run test code
  BlinkTest.ino should blink an LED.
Show your blinking LED to the course staff.

## Slide 17: TODO
Add slides for:
  Flow chart/illustrations of assembly process.
  Side view of board + paste + component.
  Problems with IMU pads being in accessible.

## Slide 18: Videos
https://www.youtube.com/watch?v=cnAFTMaS5R0