## Slide 1: Designing Packages, Symbols, and Devices

## Slide 3: Multirotor Aircraft Components
Airframe
  Structural support
  Plastic, aluminum, wood, or PCB (fiberglass)
Motors
  Lift, movement, and control
  Brushed DC motors for small craft
  Brushless brushless DC motors for large craft.
Inertial Measurement Unit (IMU)
  Sensing the aircraft’s orientation and movement
  Gyroscopes and accelerometers.
Computing resources (microcontroller/processor)
  To run the flight control software
  Manage communication
Flight control software
  Provides stability using the IMU and motors
  Converts pilot commands to motor outputs
Radio
  For receiving command
  Returning telemetry.
Power supply
  Lots of power for the motors
  Carefully regulated power for the IMU and micro controller.

## Slide 4: The Hardware You will Build

## Slide 5: The Hardware You Will Build

## Slide 6: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio

## Slide 7: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
I2C interface (more on this later)

## Slide 8: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7V
  Powers the motors directly
3.3V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU

## Slide 9: Motors and Props
DC brushed motors
2 Amps max
Plenty of power

## Slide 10: Designing Through-hole Pads
The diameter of the hole is smaller than the drilled hole
  You need to add about 0.1-0.3 mm to the desired, plated internal diameter to get the drill diameter

## Slide 11: PCB Libraries
To use a part on a PCB, you need a library entry for it
  Physical/mechanical information for the board
  Logical/electrical information for the schematic
  Mapping between the two
  Metadata
A well designed library, will make your life much, much easier.
There are lots of libraries are the internet
  Some are good, some are bad, some a poor match for what we need.

## Slide 12: Designing for Correctness
It’s very easy to introduce bugs in your library
This is no time for creativity
Copy/mimic as much as you can
  Pin names
  Pin order
  Part orientation
This minimizes errors and makes it easy to check

## Slide 13: Libraries
Libraries define the parts you can add to a PCB
Eagle libraries contain 3 different kinds of entities
  Schematic Symbols – The symbolic version of the part
  Package – The physical description of the part and how it should appear on the board
  Device – A combination of a package and a schematic

## Slide 14: Units
Units
  We will mostly use mm in this class.
  1mm is about 40mils (39.3700787, actually)
  1in is 25.4 mm.
  Keep an eye on your units.
Exceptions
  Lots of tutorials, documents, etc. use mils (1/1000 of an inch) or inches.
  Breadboards and headers are typically 0.1” spacing (2.54mm)
Mars Climate Orbiter

## Slide 15: PCB Libraries: Symbols
Schematic representation of the component
Electrical connection points – “pins”
Generic symbols: resistors, capacitors, etc.
Specific symbols: e.g., Atmega128RF
Documentation, labels, etc.
Organized for ease of use and readability

## Slide 16: Example: A Resistor Symbol
Human-readable representation of the part
Has the standard resistor “zig zag”
Two ‘pins’
  Pas 1
  Pas 2
And place holders for documentation
  >NAME – e.g. “R6”
  >VALUE – e.g. “200Ohms”

## Slide 17
Package
Symbol
Device Pin Mapping
Physical part

## Slide 18: PCB Libraries: Packages
Mechanical description of the part
Electrical connections (i.e., pads and SMDs)
Generic packages: e.g., 0805 Resistor
Specific packages: e.g., Atmegat128RF

## Slide 19: Example: A Resistor Package
Yageo RC Series SMD resistor
Package: 0805
Pads
  Extend out 1mm or so for easy soldering.
Keep out area (court yard)
  Where other parts should not be

## Slide 20: Anatomy of a Package (Resistor)
Pins
  Ex. “1” and “2”
Outline
  In tDocu (gold)
  Matches part shape precisely
Orientation/placement guidance
  in tPlace (orange)
  Varies by part.
Name
  In tNames
  Magic value “>NAME”
  See lab for font size
Value
  In tValues
  Magic value “>VALUE”
  See lab for font size
Keepouts
  In tKeepout
  Red shaded
Documentation
  In tPlace
  Other useful items

## Slide 21: Anatomy of a Package (LED)
Pins
Outline
  In tDocu (gold)
  Matches part shape precisely
Orientation/placement guidance
  in tPlace (orange)
  Mark pin 1
Name
  In tNames
  Magic value “>NAME”
  See lab for font size
Value
  In tValues
  Magic value “>VALUE”
  See lab for font size
Keepouts
  In tKeepout
  Red shaded
Documentation
  In tPlace
  Other useful items

## Slide 22: Anatomy of a Package (Microcontroller)
Pins
Outline
  In tDocu (gold)
  Matches part shape precisely
Orientation/placement guidance
  in tPlace (orange)
  Mark pin 1
Name
  In tNames
  Magic value “>NAME”
  See lab for font size
Value
  In tValues
  Magic value “>VALUE”
  See lab for font size
Keepouts
  In tKeepout
  Red shaded
Documentation
  In tPlace
  Other useful items

## Slide 23: PCB Libraries: Devices
Devices map between
  1 symbol
  >= 1 packages
For each package, the device maps the schematic pins to the package pads/SMDs.
Metadata
  “attributes” -- E.g., Manufacturer, part number, etc.
  Name prefix for reference designators -- e.g, the “R” in R1, R2, etc.
  Does it have a “value” (e.g., a resistor’s value is it’s resistance, but a microcontroller doesn’t have a value)

## Slide 24: Devices in Eagle

## Slide 25: Device Example: LED
One Symbol
Many Packages
Many Variants

## Slide 26: Example: A Resistor
The Device
Maps the symbol to the package
There can be multiple “variants”
  Different packages
  Same symbol
  Same kind of device

## Slide 27: Pads and SMDs
There are two types of connections between a PCB and a part
  “through holes” – Usually called “through holes”
  “Surface mount” – Usually called “pads” on “lands”
Eagle uses odd terminology
  ”Pads” are through hole connections
  SMD (surface mount device) are surface mount connections.

## Slide 28: The Parts
Resistor
LED
MOSFET
IMU

## Slide 29: Datasheets
Datasheets describe electronic component.
Capabilities
Mechanical information
  Size
  Recommended board layout
  Pin location
Electrical information
  Input/output voltages
  Additional required components
Schematic Applications
  Examples of how to connect the part electrically
Processing information
  Reflow soldering requirements
  Packaging information

## Slide 33: Tech Notes
More detailed information on some aspect of a part.
They will usually be referenced in the data sheet.
Sometimes, you just need to go looking for them.

## Slide 35: The LEDs
Draw an appropriate symbol (look online for examples)
Pay careful attention to orientation.
Do not confuse the cathode and the anode
Correct orientation should be clear on the schematic symbol and the package.

## Slide 36: MOSFET
Symbol
  It’s an NMOS transistor
  Use google to find an appropriate symbol
  Make sure you get the source and drain correct (follow the datasheet)
Package
  We need large metal pads for thermal reasons
  But small pads.
  Pads with large metal/small solder mask opening

## Slide 37: MOSFET Pad guidance in the datasheet

## Slide 38: Demo and Lab Walk Through
Mosfet
  Symbol
  Package
  Device
IMU
  Symbol
  Package
  Device