## Slide 1: Agenda For today
Questions from ”readings”
Project Overview
Lab Overview

## Slide 2: PCB Libraries: Packages, Symbols, and Devices
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 3: Designing for Correctness
Building correct libraries can be hard
  It’s very easy to introduce bugs in your library
  It can be very hard to find bugs in your library.
Your goal is to make it as easy as possible to verify your library’s correctness
Copy/mimic the datasheet as much as you can
  Pin names
  Pin order
  Part orientation
This minimizes errors and makes it easy to check

## Slide 4: PCB Libraries
To use a part on a PCB, you need a library entry for it
  Physical/mechanical information for the board
  Logical/electrical information for the schematic
  Mapping between the two
  Metadata
A well-designed library, makes your life much, much easier.
There are lots of libraries are the internet
  Some are good, some are bad, some a poor match for what we need.

## Slide 5: PCB Libraries: Symbols
Schematic representation of the component
Electrical connection points – “pins”
Generic symbols: resistors, capacitors, etc.
Specific symbols: e.g., Atmega128RF
Documentation, labels, etc.
Organized for ease of use and readability
Battery
Resistor
LED
Our voltage regulator

## Slide 6: Example: A Resistor Symbol
Human-readable representation of the part
Has the standard resistor “zig zag”
Two ‘pins’
  Pas 1
  Pas 2
And place holders for documentation
  >NAME – e.g. “R6”
  >VALUE – e.g. “200Ohms”

## Slide 7: PCB Libraries: Packages
Mechanical description of the part
  Electrical connections (i.e., pads and SMDs)
  ”keepouts” (i.e., the space the occupy)
  Documentation (e.g., an outline to guide placement, reference designators, user documentation)
Generic packages
  e.g., 0805 Resistor (there are 1000s of kinds of these)
Specific packages
  e.g., Atmegat128RF (there’s just one kind)
An “chip” antenna
Standard SOT23 package
Programming Header

## Slide 8: The Fusion360 Command Line
You can use your mouse to select tools in Fusion, but it’s slow.
Faster is to type commands using the command line
You can mouse of the tool pallet to get the command name
  e.g., “move”, “copy”, ”info”, …
Then type ‘help <name>’ for help.
Or just type the name to select that tool.
This will save you hours over the course of the quarter.

## Slide 9: Units
Units
  We will mostly use mm in this class.
  1mm is about 40mils (39.3700787, actually)
  1in is exactly 25.4 mm.
  Keep an eye on your units.
Exceptions
  Fusion schematic symbols and schematics use inches
  Lots of tutorials, documents, etc. use mils (1/1000 of an inch) or inches.
  Breadboards and headers are typically 0.1” spacing (2.54mm)
Mars Climate Orbiter

## Slide 10: Working with Units in Fusion
Use the “grid” tool (or command) to set grid Fusion will “snap” to.
‘grid mm’ -> switch to mm
‘grid 1’ -> make the grid 1 of the current unit

## Slide 11: Example: A Resistor Package
Yageo RC Series SMD resistor
Package: 0805 (8mm x 5mm)
Pads
  Extend out 1mm or so for easy soldering.
Keep out area (courtyard)
  Where other parts should not be
Yageo makes these in many sizes 0075 (so tiny!) to 0805

## Slide 12: Anatomy of a Package (Resistor)
Pins
  Ex. “1” and “2”
Outline
  In tDocu (gold)
  Matches part shape precisely
Orientation/placement guidance
  in tPlace (orange)
  Varies by part.
Name
  In tNames
  Magic value “>NAME”
  See lab for font size
Value
  In tValues
  Magic value “>VALUE”
  See lab for font size
Keepouts
  In tKeepout
  Red shaded
Documentation
  In tPlace
  Other useful items

## Slide 13: Anatomy of a Package (LED)
Same basic parts as a resistor.
But LEDs are not reversible.
Polarity marking
  in tPlace (orange)
  Mark pin 1

## Slide 14: Anatomy of a Package (Microcontroller)
Same components, just more pins

## Slide 15: A Note about tKeepout
Carefully designed tKeepout + a 0.5 mm placement grid is what makes laying out the board easy(ish).
Draw tkeepout on a 0.5mm grid
Keep tkeepout lines i.e., more than 1.25 grid squares but less than 2.25 from the SMDs and package bodies (or so).
  Don’t obsess about these numbers.
  You can “hug” the pins and package if you want.
Then inset it by 0.1mm
  Set grid 0.1mm and move each line segment in 0.1mm
  Fiddly but worth it.

## Slide 16: tKeepout Example
Initial layout
Inset

## Slide 17: tKeepout Example

## Slide 18: PCB Libraries: Devices and Variants
There is one “device” in a library for each kind of electrical component
  Resistor
  Capacitor
  AtmegaRFA128 microcontroller
Each device can have several “variants” (Fusion term)
There’s one variant for each specific electrical component
  Yageo AC0603JR-07510RL (510 Ohm resistor)
  Yageo AC0603JR-072K2L (2.2KOhm resistor)
  …
Variants are what you add to your design.

## Slide 19: PCB Libraries: Devices & Variants
Devices map between
  1 symbol
  1 or more variant
A variant has
  Name
  Package
  Pin mapping
  Metadata
    “attributes” -- e.g., manufacturer, part number, resistance, capacitance
    Name prefix for reference designators -- e.g., the “R” in R1, R2, etc.
    Does it have a “value”? (e.g., a resistor’s value is its resistance, but a microcontroller doesn’t have a value)

## Slide 20: Device Example: LED
One Symbol
Many Packages
Many more variants

## Slide 21: Symbol-to-Package Mapping & Metadata
Attribute | Value
Part Number | XAU252ae-22
Manufacture | LED Inc.
Package
Symbol
Physical part

## Slide 22: Example: A Resistor

## Slide 23: Connecting Symbol Pins to Package Pads

## Slide 24: PCB Libraries: Packages, Symbols, and Devices
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 26: Building Parts in Fusion Lab Overview
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 27: A Note about tKeepout (The video doesn’t cover this enough)
Carefully designed tKeepout + a 0.5 mm placement grid is what makes laying out the board easy(ish).
Draw tkeepout on a 0.5mm grid
Keep tkeepout lines i.e., more than 1.25 grid squares but less than 2.25 from the SMDs and package bodies (or so).
  Don’t obsess about these numbers.
  You can “hug” the pins and package if you want.
Then inset it by 0.1mm
  Set grid 0.1mm and move each line segment in 0.1mm
  Fiddly but worth it.

## Slide 28: tKeepout Example
Initial layout
Inset

## Slide 29: tKeepout Example

## Slide 30: The Parts You Will Build
Resistor
LED
MOSFET
IMU

## Slide 31: Datasheets
Datasheets describe electronic component.
Capabilities
Mechanical information
  Size
  Recommended board layout
  Pin location
Electrical information
  Input/output voltages
  Additional required components
Schematic Applications
  Examples of how to connect the part electrically
Processing information
  Reflow soldering requirements
  Packaging information

## Slide 38: Tech Notes
More detailed information on some aspect of a part.
They will usually be referenced in the data sheet.
Sometimes, you just need to go looking for them.

## Slide 39: IMU Tech Notes
There are two of them in the Datasheet directory.
  IMU_*
One is about LGA soldering
The other is about soldering sensors in particular.
Read them!

## Slide 40: MOSFET
An electrically controlled switch
It controls the large currents to the motors
Symbol
  It’s an NMOS transistor
  Use google to find an appropriate symbol
  Make sure you get the source and drain correct (follow the datasheet)
Package
  We need large metal pads for thermal reasons
  But small bits of exposed metal for soldering
  Pads with large metal/small solder mask opening

## Slide 41: MOSFET Pad guidance in the datasheet
Solder mask openings
Metal pads

## Slide 42: The LEDs
You will design your LED from scratch!
Draw an appropriate symbol (look online for examples)
Pay careful attention to orientation.
Do not confuse the cathode and the anode
Correct orientation should be clear on the schematic symbol and the package.

## Slide 43: Questions?

## Slide 44: Demo and Lab Walk Through
MOSFET
  Part generator
  Symbol
  Package
  Device
IMU
  Symbol
  Package
  Device

## Slide 45: Next time
Lecture was about 30 minutes of questions + 1 hour of new material.

## Slide 46: Building a PCB Footprint Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 47: Building a PCB Schematic Symbol Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 48: Building a PCB Device Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu