## Slide 1: Next time
Add slide about nicely laying out schematic
Talk about layers
Remember to talk about decoupling
And GND, BAT_GND, and the bridge

## Slide 3: Designing Nice Schematics
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 4: Schematic Layers in Eagle
Eagle (and other tools) use layers to for different schematic information.
  Nets – wires (electrical connections)
  Pins – Connection points on symbols
  Symbols – symbols
  Names – symbol and pin names
  Values – symbol values (e.g., resistance for resistors)
  Info – Documentation
  We won’t use the others

## Slide 5: Demo
Show what’s in each of the layer
Good Schematic style
Bad Schematic Style
Eagle Pitfalls

## Slide 6: Building The Quadcopter Schematic

## Slide 7: Schematics Goals
Determine what components your PCB will hold
Define the electrical connectivity between those components
Specify some metadata about the parts

## Slide 8: Eagle Pitfalls
Always edit schematics with your grid set to 0.1” or 0.05” – ALWAYS!!!
Wires/pins can look connected but not be.
  ‘Wiggle’ parts to make sure wires move with them.
  Check for the green dot.

## Slide 9: Electrical Rules Check
This checks for common problems in schematics.
Make sure you understand the reason for the errors.
Fix them if you can.
Run it!

## Slide 10: The Hardware You will Build

## Slide 11: The Hardware You Will Build

## Slide 12: Three Schematic Design Skills
Copy – You will manually copy the microcontroller circuit from a small breakout board that uses the same MCU.
Copy – you’ll copy the motor controller based on a schematic I provide.
Implement – You will look at the data sheet for the IMU and voltage regulator and implement the design it provides.
Design – you will add some LEDs to your design on your own.

## Slide 13: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7-4.2V
  Powers the motors directly
3.3V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU

## Slide 14: Voltage Regulator Datasheet

## Slide 15: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 16: uController Datasheet and Reference Design

## Slide 17: Decoupling Capacitors

## Slide 18: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
We will use the I2C interface

## Slide 19: Why I2C?
Pins are precious!
  They take up space
  More pins  More expensive microcontrollers
  Adding pins is hard
    Might need a new microcontroller (if a larger, compatible one is available)
    Significant board changes
Performance is often not that important
So
  Use the minimum number of pins
  Run them at relatively low bit rates.

## Slide 20: I2C Bus Architecture
Two signals
  SCL – Serial Clock (used for coordination and timing)
  SDA – Serial Data (used for data and control signaling)
  Both pulled up to VCC via a large resistor (e.g. 10 kΩ)
Two I2C roles
  A master that initiate communication (The MCU)
  Up to 127 slaves that can respond (The IMU)
Two operations: Read and write
  The master can read and write registers specified by an address.

## Slide 21: IMU Datasheet
Sections 4 and 5-5.1

## Slide 22: Motors and Props
Plenty of power
DC brushed motors
They draw ~2A each.

## Slide 23: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it turns off (“flyback”)
Pull down resistor so it defaults to ‘off’.

## Slide 24: Pulse Width Modulation
Motor speed varies with voltage
Varying the voltage directly is hard
PWM varies the average voltage using a digital signals
  Duty cycle: % of time signal is high
  Cycle time: delay between rising edges (2ms on our MCU)
  Frequency: 1/Cycle time (490Hz)
Our MCU has hardware for this
  Accessed via analogWrite()
  Cycle time = 2ms
  Frequency = 490Hz

## Slide 25: Motor Switching: Inductance and Flyback
Inductance -- Resistance to a change in current
  Current takes time to start and stop flowing.
  Imagine water flowing in a pipe when you turn off the faucet.
Formally, changing current (I) creates a voltage (VL) proportional to the rate of change and the inductance (L)

## Slide 26: Motor Switching: Inductance and Flyback
Motors are inductors (and resistors)
Motor voltage equation
  Vm = voltage across the motor
  I = Motor current
  R = Motor resistance
  L = Motor Inductance
  dI/dt = rate of change of motor current

## Slide 27: Motor Switching: Inductance and Flyback
Add a ‘fly back diode’
When the switch is closed
  No effect (reverse-biased)
When the switch is closed
  Forward-biased
  Routes current back into the motor
Good videos
  https://www.youtube.com/watch?v=6R_3jHeimiE
  https://www.youtube.com/watch?v=m5JYkgCRbBI&t=1s

## Slide 28: LEDs
You will add some LEDs to you quadcopter.
Three steps
  Design your lighting scheme
  Pick them on Digikey.com
  Design the circuit to control them

## Slide 29: LED Design
Functional
  Which way is forward?
  Status information
Pretty
  Ground effects
  Display your quad’s mood
Options
  “indicator” LEDs draw a few mA
  “lighting” LEDs can draw up to several amps.
Constraints
  0.5 A maximum across all your LEDs

## Slide 30: LED Selection
There are lots of LED
You will pick them on digikey
  Must be at least 0805 (2mm x 1.25mm)
  Available in quantities of 1
  Cost < $1 per LED

## Slide 31: LED Datasheets
Key device parameters
  Forward voltage: Vf
  Color
  Luminous intensity
Key absolute limits
  Forward current

## Slide 32: LED Circuit design
Ohm’s Law : V = IR
The forward voltage (Vf) across an LED is (roughly) fixed
Driving the LED at > Vf will burn it out.

## Slide 33: Limiting Current
Ohm’s Law : V = IR
The forward voltage (Vf) across an LED is (roughly) fixed
Add a resistor to limit current.

## Slide 34: Set Your Brightness Carefully
Indicator LEDs do not need to be driven hard
The red LED on the FCB uses a 510Ω resistor
  Vf = 2V; Vcc = 3.3
  I = V/R => I = (3.3-2.0)/510 = 2.5mA
  The maximum brightness (@30mA) is 12x higher
  They can easily become blindingly bright.

## Slide 35: Controlling your LEDs
Drive directly with MCU pin
  Good for indicators
  < 10mA/LED
  Use a PWM pin to make them dimmable
Drive via MOSFET (digital or PWM)
  Good for bright LEDs
  <500mA total.
You can run several LEDs in series if Vf is low enough.
You can run them in parallel too, but brightness will vary.
You can also just wire them to power.

## Slide 36: Turning in your LED design
Pick your LEDs
Commit your datasheets
Create the Eagle library (including any resistors your need)
Add led_notes.txt, explaining your design.

## Slide 37: Demo
Schematic organization
Connection via named nets
Using ‘show @’ to check connectivity
Explain how Eaglint checks things (path based patterns).

## Slide 38: Building a Schematic Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu