## Slide 1: Building The Quadcopter Schematic

## Slide 2: Schematics Goals
Determine what components your PCB will hold
Define the electrical connectivity between those components
Specify some metadata about the parts

## Slide 3: Eagle Pitfalls
Always edit schematics with your grid set to 0.1” or 0.05” – ALWAYS!!!
Wires/pins can look connected but not be.
  ‘Wiggle’ parts to make sure wires move with them.
  Check for the green dot.

## Slide 4: Electrical Rules Check
This checks for common problems in schematics.
Make sure you understand the reason for the errors.
Fix them if you can.
Run it!

## Slide 5: Building The Quadcopter Schematic

## Slide 6: What You Will Build

## Slide 7: What You Will Build

## Slide 8: Three Schematic Design Skills
Copy – You will manually copy the microcontroller circuit from the BBB.
Copy – you’ll copy the motor controller based on a schematic I provide.
Implement – You will look at the data sheet for the IMU and voltage regulator and implement the design it provides.
Design – you will add some LEDs to your design on your own.

## Slide 9: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7-4.2V
  Powers the motors directly
3.3V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU

## Slide 10: Voltage Regulator Datasheet

## Slide 11: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 12: uController Datasheet and Reference Design

## Slide 13: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
We will use the I2C interface

## Slide 14: Why I2C?
Pins are precious!
  They take up space
  More pins  More expensive microcontrollers
  Adding pins is hard
    Might need a new microcontroller (if a larger, compatible one is available)
    Significant board changes
Performance is often not that important
So
  Use the minimum number of pins
  Run them at relatively low bit rates.

## Slide 15: I2C Bus Architecture
Two signals
  SCL – Serial Clock (used for coordination and timing)
  SDA – Serial Data (used for data and control signaling)
  Both pulled up to VCC via a large resistor (e.g. 10 kΩ)
Two I2C roles
  A master that initiate communication (The MCU)
  Up to 127 slaves that can respond (The IMU)
Two operations: Read and write
  The master can read and write registers specified by an address.

## Slide 16: IMU Datasheet
Sections 4 and 5-5.1

## Slide 17: Motors and Props
Plenty of power
DC brushed motors
They draw ~2A each.

## Slide 18: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it turns off (“flyback”)
Pull down resistor so it defaults to ‘off’.
Large capacitor for “decoupling”

## Slide 19: Pulse Width Modulation
Motor speed varies with voltage
Varying the voltage directly is hard
PWM varies the average voltage using a digital signals
  Duty cycle: % of time signal is high
  Cycle time: delay between rising edges (2ms on our MCU)
  Frequency: 1/Cycle time (490Hz)
Our MCU has hardware for this
  Accessed via analogWrite()
  Cycle time = 2ms
  Frequency = 490Hz

## Slide 20: Motor Switching: Inductance and Flyback
Inductance -- Resistance to a change in current
  Current takes time to start and stop flowing.
  Imagine water flowing in a pipe when you turn off the faucet.
Formally, changing current (I) creates a voltage (VL) proportional to the rate of change and the inductance (L)

## Slide 21: Motor Switching: Inductance and Flyback
Motors are inductors (and resistors)
Motor voltage equation
  Vm = voltage across the motor
  I = Motor current
  R = Motor resistance
  L = Motor Inductance
  dI/dt = rate of change of motor current

## Slide 22: Motor Switching: Inductance and Flyback
Add a ‘fly back diode’
When the switch is closed
  No effect (reverse-biased)
When the switch is closed
  Forward-biased
  Routes current back into the motor
Good videos
  https://www.youtube.com/watch?v=6R_3jHeimiE
  https://www.youtube.com/watch?v=m5JYkgCRbBI&t=1s

## Slide 23: LEDs
You will add some LEDs to you quadcopter.
Three steps
  Design your lighting scheme
  Pick them on Digikey.com
  Design the circuit to control them

## Slide 24: LED Design
Functional
  Which way is forward?
  Status information
Pretty
  Ground effects
  Display your quad’s mood
Options
  “indicator” LEDs draw a few mA
  “lighting” LEDs can draw up to several amps.
Constraints
  0.5 A maximum across all your LEDs

## Slide 25: LED Selection
There are lots of LED
You will pick them on digikey
  Must be at least 0805 (2mm x 1.25mm)
  Available in quantities of 1
  Cost < $1 per LED

## Slide 26: LED Datasheets
Key device parameters
  Forward voltage: Vf
  Color
  Luminous intensity
Key absolute limits
  Forward current

## Slide 27: LED Circuit design
Ohm’s Law : V = IR
The forward voltage (Vf) across an LED is (roughly) fixed
Driving the LED at > Vf will burn it out.

## Slide 28: Limiting Current
Ohm’s Law : V = IR
The forward voltage (Vf) across an LED is (roughly) fixed
Add a resistor to limit current.

## Slide 29: Set Your Brightness Carefully
Indicator LEDs do not need to be driven hard
The FCB uses 330Ω resistor
  Vf = 2.1V; Vcc = 3.3
  I = V/R => I = (3.3-2.1)/330 = 3mA
  The maximum brightness (@30mA) is 16x higher
  They can easily become blindlingly bright.
Remote
  Vf = 2.1V/2.0V; Vcc = 3.3
  R = 510Ω
  I = 2mA
  Still plenty bright.

## Slide 30: Controlling your LEDs
Drive directly with MCU pin
  Good for indicators
  < 10mA/LED
  Use a PWM pin to make them dimmable
Drive via MOSFET (digital or PWM)
  Good for bright LEDs
  <500mA total.
You can run several LEDs in series if Vf is low enough.
You can run them in parallel too, but brightness will vary.
You can also just wire them to power.

## Slide 31: Turning in your LED design
Pick your LEDs
Commit your datasheets
Create the Eagle library (including any resistors your need)
Add led_notes.txt, explaining your design.

## Slide 32: Demo
Schematic organization
Connection via named nets
Using ‘show @’ to check connectivity
Explain how Eaglint checks things (path based patterns).

## Slide 33: Next time
Add slide about nicely laying out schematic
Talk about layers
Remember to talk about decoupling
And GND, BAT_GND, and the bridge.