## Slide 1: Building The Quadcopter Schematic

## Slide 2: Schematics Goals
Determine what components your PCB will hold
Define the electrical connectivity between those components
Specify some metadata about the parts

## Slide 3: Schematic Example
open /Users/swanson/UCSD/Teaching/18sp-190/QuadClass-Resources/Lecture\ Slides/Examples/ATmega128RFA1-DevBoard/ATmega128RFA1-DevBoard.sch

## Slide 4: Eagle Pitfalls
Always edit schematics with your grid set to 0.1” or 0.05” – ALWAYS!!!
Wires/pins can look connected but not be.
  ‘Wiggle’ parts to make sure wires move with them.
  Check for the green dot.

## Slide 5: Electrical Rules Check
This checks for common problems in schematics.
Make sure you understand the reason for the errors.
Fix them if you can.
Run it!

## Slide 6: Building The Quadcopter Schematic

## Slide 7: What You Will Build

## Slide 8: What You Will Build

## Slide 9: Three Schematic Design Skills
Copy – You will manually copy the microcontroller circuit from the remote.
Copy – you’ll copy the motor controller based on a schematic I provide.
Implement – You will look at the data sheet for the IMU and voltage regulator and implement the design it provides.
Design – you will add some LEDs to your design on your own.

## Slide 10: Power Supply
Lithium Polymer Battery
  370 Mah
  Max 9.25 Amps
  Nominal voltage = 3.7-4.2V
  Powers the motors directly
3.3V low dropout (LDO) voltage regulator
  Powers the microcontroller and the IMU

## Slide 11: Regulator Datasheet

## Slide 12: Flight Computer
ATmega128RFA1 microcontroller
  Arduino compatible
  16Mhz clock
  128KB Flash
  16KB SRAM
  4096B EEPROM
  2.4GHz radio (Compatible with Zigbee)

## Slide 13: uController Datasheet and Reference Design

## Slide 14: Inertial Measurement Unit
STMicro LSM9DS1
9-axis sensor
  3-axis accelerometer
  3-axis magnetometer
  3-axis gyroscope
We will use the I2C interface

## Slide 15: IMU datasheet
Notes
  You can tie all the RES/GND pads to one pin on the schematic symbol

## Slide 16: Motors and Props
Plenty of power
DC brushed motors
They draw ~2A each.

## Slide 17: Motor Switching: Inductance and Flyback
Inductance
  Resistance to a change in current
Intuitively, current takes time to start and stop flowing.
  Imagine water flowing in a pipe

## Slide 18: Motor Switching: Inductance and Flyback
Motors are inductors (and resistors)
Motor voltage equation
  Vm = voltage across the motor
  I = Motor current
  R = Motor resistance
  L = Motor Inductance
  dI/dt = rate of change of motor current

## Slide 19: Motor Switching: Inductance and Flyback
Add a ‘fly back diode’
When the switch is closed
  No effect (reverse-biased)
When the switch is closed
  Forward-biased
  Routes current back into the motor
Good videos
  https://www.youtube.com/watch?v=6R_3jHeimiE
  https://www.youtube.com/watch?v=m5JYkgCRbBI&t=1s

## Slide 21: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.
A diode handles the inductive load from motor when it’s off.