## Slide 1: Implementing PID
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 2: To add
Discuss different ways they can control their quad
  Pitch/roll -> rate of change of angle
  Pitch/roll -> angle of attack
  Pitch/roll -> velocity
  Pitch/roll -> position
  Throttle -> throttle
  Throttle -> rate of climb
  Throttle -> altitude
Discuss higher-order control
  How to integrate GPS
  How to integrate barometer

## Slide 3: Control Theory Basics
Making a physical system do what you want
Open loop - cannot see the system’s output
  Motor controllers
  LCD/LED/CRT screens
Closed loop – measures output, make corrections
  Autopilot
  Cruise control
  Our quadcopter

## Slide 4: PID: The Usually-Good-Enough Controller
Make a system follow a set point
“Proportional, Integral, Derivative”
A brief history:
  1788 - James Watt’s flyball governor (P)
  1837 - Louis Molinié hydraulic regulator (PI)
  1857 - H.N. Throop marine engine governor (PD)
  1911 - Elmer Sperry, ship steering (PID)

## Slide 5: PID Details
PID is the most common closed loop controller
Proportional: Directly correct error
Integral: Account for steady-state error
Derivative: Dampens response, avoids overshoot

## Slide 6: Example
https://sites.google.com/site/fpgaandco/pid

## Slide 7: This Lab
Implement a mechanism to tune the PID values from your remote
Implement and tune PID for Yaw
  You yaw stick on the remote should control the yaw rate
  You can use the gyro output directly.
Implement and tune PID for Pitch
  Your Pitch stick should control the pitch angle
  Use the output of your complimentary filter
Demonstrate that you have achieved control hanging upside (yaw) or on the test stand (pitch)

## Slide 8: Implementation
NOTES:
  Where to get the derivative?
  Integral windup
  Pay attention to rate (hz)
  Relative scale of inputs and outputs
    Should you include the time step?
    Make sure timestep is consistent

## Slide 9: How important in speed?
The key number is how many times/sec your PID loops (Hz)
The internet suggests > 100Hz (10ms/cycle) is necessary for stable flight.
My non-optimized code runs at 400Hz (2.5ms/cycles)
Action | Latency (ms)
Reading IMU | 7.360
analogWrite() | 0.012
analogRead() | 0.104
Integer PID (one channel) | 1.880 (531Hz)
FP PID (one channel) | 1.888 (529Hz)
AHRS getOrientation() | 1.860
rfWrite() 16 bytes | 0.812
Serial.write(“a”) | 0.906

## Slide 10: Remote Software Path
Scale gimbal readings (-512-512 for P,R, Y; 0-1023 for T)
“deadband” avoids noise near the mid point.
Performance is not critical 10-20Hz updates is more than enough.

## Slide 11: Quadcopter Datapath

## Slide 12: The Mixer
Keep it simple
Set all motor outputs to the throttle
Add and subtract your PID values for each axis
  Do it symmetrically so that the other axes are not affected
  E.g., Adjust pitch by adding one CW and one CCW motor and subtracting from on CW and CCW motor

## Slide 13: Tuning Suggestions
Tuning Order
  Tune P – there will be a lot of oscillation and bouncing around on the test stand
  Tune D – Dampen the oscillation
  Tune I – remove offset error (beware the windup)
Reading the oscillation
  Get a feel for the rate of oscillation you see with just P.
  Higher-frequency oscillation is usually too much D.
  Lower-frequency oscillation is usually too much I.
Higher P and I values tend to increase responsiveness
  It reacts more aggressively to error
Higher D values tends reduce responsiveness
  It can “overdamp” the the quadcopter and prevent it from reaching the set point.

## Slide 14: PID Pitfall: Integral Windup
The integral term accumulates error
If error is large for a long time, this value can grow very large
Possible causes (among others)
  If I is 0, the quad won’t correct for steady-state error, so that error will accumulate
  If the motors are off, the quad won’t correct error, so it will grow.
  If you hold the quad so it can’t move, the sum will grow.
Solutions
  Have the integral decay over time (sum = sum/2 + Error)
  Reset sum to 0 when the throttle is off.

## Slide 15: PID Pitfall: Derivative Noise
The D terms is susceptible to noise
Configure your IMU filters wisely
Error term with vibration
Derivative term goes crazy

## Slide 16: PID Pitfall: Complexity
Your PID implementation does not need to be complicated.
Simplicity is your friend.
So is careful debugging.
Assume nothing!
My PID Implementation
My Complimentary filter Implementation

## Slide 17: PID Pitfall: Not Preparing Your Infrastructure
Invest in debugging and monitoring code
It will save you loads of time
For instance
  Make your data easily plottable
  Make it easy to configured what’s plotted
  Make your remote easy to use
  Send useful telemetry.
  Make it easy to adjust filter tuning.
  Save PID values to EEPROM
  Make it easy re-check the basics
    IMU measurements
    Filter output
    Calibration
My Complimentary filter Implementation
Debugging Code

## Slide 18: PID Pitfall: Taking too Long
If your loop() takes too long, PID response will be sluggish.
Your loop rate should be something near 100Hz (10ms/iteration)
Possible causes
  Too much Serial.print()
  To many packets (they cause interrupts)
  To much complex math.
Solutions
  Increase serial port rate (at least 115200 should be possible)
  Have your remote transmit no more than 10 times per second.
  Track your loop rate with millis().

## Slide 19: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 20: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 21: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 22: Yaw Axis PID Checklist
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 23: Pitch Axis PID Tuning and Checklist
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu