## Slide 1: Introduction To Printed Circuit Boards
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 2: PCB Overview
PCBs provide electrical connectivity
  Compact
  Mass-manufacturable
  Durable
  Reliable
They comprise (usually) copper wires embedded in a composite matrix
Electrical components are soldered to one or both surfaces.
They are everywhere!
  Many PCBs are easy to design and manufacture.
  The board is ~$2 of that
  The FCB cost $50 fully assembled in lots of 25
There’s no upper limit on cost or sophistication

## Slide 3: PCBs are Made of Layers
Silkscreen – documentation and labels
Metal – for making wires
Dielectric – insulation and mechanical structure
Solder mask – protective outer coating

## Slide 4: Metal Layers
The Metal layers
  Conductive “traces” to connect components
  Attaching components
More layers  more expensive
Top and bottom layers are for mounting components and routing traces
Internal layers can serve several purposes
  Ground and power planes
  Other signal planes
  Internal routing layers

## Slide 5: Metal Layers (cont.)
Thickness is measured in oz per square foot.
Standard copper is 1oz
  About 0.034 mm

## Slide 6: Dielectric
The dielectric is the insulator between metal layers
Most PCBs use FR4
  “glass reinforced epoxy laminate”
  i.e., fancy fiberglass
  “FR” means “flame retardant”
Other specialized dielectrics are are available
  To support high speed circuits
  To manage thermal expansion
Bare FR4

## Slide 7: Solder Mask
Plastic coating on the top and bottom of the board
Protects the top and bottom metal from oxidation.
Helps prevent solder bridges
Gives the board color

## Slide 8: Silkscreen
It’s an opaque, (usually) white epoxy or polymer
It provides documentation and markings
  References designators
  Part outlines
  Logos
  Serial numbers etc.

## Slide 9: Making Connections Between Layers
Metal-plated holes connect metal layers.
Drill a hole
Electroplate it with copper
Cover it with a non-corroding metal.

## Slide 10: Connecting Wires with “Vias”
Vias make electrical connections between layers
They are usually very small.
Often covered by solder mask
Typically, they pass through all layers

## Slide 11: Mounting Components with Through-holes
Through-hole “pads”
  Sized for the pin + solder
  Significantly larger than vias
Draw backs
  Takes up space in all layers (including back side of board)
  Pin-to-pin spacing >= 1mm
  Automated manufacturing is challenging

## Slide 12: Surface Mount Devices (SMD)
No drill required
No pins
Smaller parts
Finer ‘pitch’ (pin-to-pin distance)
Parts on both sides
Easier automated placement
Pitch >= ~0.3 mm

## Slide 14: Lots of Choices, in Theory
There are many, many choices when designing a PCB
  Mechanical – flexible, thick, thin
  Layer count
  Blind and buried vias
  Electrical – copper thickness, dielectric characteristics
  Thermal characteristics
We will get to make very few of them
Cheap, fast PCB manufacturers provide a standard setup. E.g.:
  FR4
  1oz copper
  2, 4, or 6 layers
  A few solder mask colors

## Slide 15: Resources
Good PCB manufacturing videos
  https://www.youtube.com/playlist?list=PL8zP8UuDk8a0ZNWiteC-7PHx1HCeBY0qB

## Slide 17: Designing PCBs
Dr. Steven Swanson
CSE176e/276e

## Slide 18: Steps for Designing PCBs
Create/acquire a library of components
Assemble your schematic
Lay out the board
Perform design checks
Generate CAM files
Check everything carefully
Submit for manufacturing

## Slide 19: PCB Libraries
PCB Libraries tell the PCB design software about physical components
Engineering data
  What kind of component is it?
  What electrical connections does it have?
  How will it connect to the PCB?
  How should it appear on the PCB?
Manufacturing data
  What is the part number?
  Where can I purchase it?
  …

## Slide 20: A Simple LED
Attribute | Value
Part Number | XAU252ae-22
Manufacture | LED Inc.
The physical Part
Schematic Symbol
PCB “Footprint”
A “Device”

## Slide 21: PCB Library
One Symbol
Many Packages
Many Parts

## Slide 22: The Library
Package
Symbol
Device Pin Mapping
Physical part

## Slide 23: Schematics
Schematics define the electrical connections between parts
It abstracts away everything mechanical about the design
  e.g., all resistors look the same
  Size is not important
  Location is not important
Schematic priorities
  Correctness, readability, clarity

## Slide 24: PCB Layout
The layout maps the schematic to a physical thing
  Symbols -> Footprints
  Wires -> copper traces
The size, shape, and location matter
Layout priorities
  Correctness (electrical + mechanical)
  Manufacturability
  Tidiness
  Readability

## Slide 25: Schematic vs. Board

## Slide 26: Designing with Layers
Eagle (and other board design tools) use layers to specify different types of information about a design.
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52(!) layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 27: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 28
Top (metal)
Bottom (Metal)
Drills (pads + vias)
tNames (top part names)
Pads (through-holes)
tPlace (top silkscreen)

## Slide 29: Useful Layer Commands
“display <layer>” -- show the layer
“display -<layer>” – hide the layer
“display last” return to previous view
Click and hold the layer tool icon to get a list of present layers sets.
  Select “new…” to save the current view
  Then “display foo” to switch to the view named “foo”

## Slide 30: Manufacturing
Eagle layers are partly Eagle-specific
  Some are semantic
  Some are documentary
  Some correspond to physical layers
Boards manufactures need
  Metal layers
  Silkscreen
  Soldermask
  Drills
  All in a standard format

## Slide 31: Computer Aided Manufacturing (CAM) Files: Gerbers
Eagle’s CAM processor generates CAM files
  “Gerbers” – precise drawings of the physical layers.
  “Drill file” – Where to drill the holes
Manufacturing Requirements
  Minimum drill size
  Minimum feature width
  File formats and names
  Our manufacturer: https://www.pcbcart.com/pcb-fab/standard-pcb.html
Our configuration encodes their requirements
  QuadClass-Resources/Eagle/DRU/pcbcart-4layer.cam

## Slide 32: Submitting for Manufacturing
Ordering PCBs is easy
Make a zip file of your gerbers
Upload it select some options
  Quantity
  Board thickness
  Solder mask color
  Board size.
  Layer count
They will check your design
Boards arrive in ~1 week

## Slide 33: Eagle Lint
A “lint” tool:
  Tool to check coding standards and other invariants about a system.
Eaglint will check your libraries, schematics
  Check for correctness
  Check for style
Also checks for other files in your repo
  Eaglint will tell you what it’s looking for.
  Pay attention.
Provides a workflow for me to review your designs and provide feedback.
To use
  Visit http://eaglint.nvsl.io
  You received a welcome email a couple of nights ago.

## Slide 34: Eagle Lint Process
Commit and push your changes to github
Submit your repo to Eaglint for a quick check
Submit your repo to Eaglint for a full check
If warnings/errors
  Fix and goto 1.
Submit for human review
If rejected
  Read comments; goto 1.
Else if accepted
  Goto next lab

## Slide 35: Eaglint Demo

## Slide 36: Grading on PCB Labs
The key to PCB design is attention to detail.
  Building a real board can take 4 months.
  If you make a mistake, it takes 4 months to fix.
    Contrast to software: just recompile and rerun!
  Don’t make any mistakes! Check your work!
Grading for PCB labs
  A “perfect” score is 10 points
  You start out with 11-12 points (depending on the lab).
  Every time you submit a design to Eaglint, you lose 0.5 point.
  Every time you submit a design for human review Eaglint, you lose 0.5 point.
  You must complete the labs.
“Quick checks” are free.

## Slide 38: Designing PCBs with Eagle AutoDesk Fusion 360

## Slide 39: Naming Confusion
We used to use “Eagle” to design PCBs
Eagle was purchased by AutoDesk
Integrated into their Fusion360
So ”Fusion”, “Fusion 360”, and “Eagle” all mean the same thing.
I don’t know how well the transition to Fusion 360 will go.

## Slide 40: Fusion Tips and Tricks
Setting the grid
Making lines straight

## Slide 41: Next time:
Major points of confusion in this lab
  How to set and align to grid
  How to make wires straight
  Where to look for the SMD location in the button datasheet
  Adafruit tutorial is not consistent with our guidance

## Slide 42: The Lab
Use Fusion to design a simple schematic and board.
Run it through the tool flow.
Submit it through Eaglint

## Slide 43: Fusion uses odd terminology
”Pads” are through hole connections
SMD (surface mount device) are surface mount connections.