## Slide 1: Laying Out the Board
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 2: Board Layout Goals
Mechanical constraints – Some things need to be in specific locations
Electrical constraints – Does the layout meet signal integrity/EM requirements
  Will digital interference mess up the antenna?
  Are decoupling caps near IC Supply pins?
  Keep the noisy power/ground for the motors away from the digital logic.
Correctness – things don’t overlap or hang off the board.
Ease of routing – Connected items should be physically close.
Make it pretty – you want a nice-looking board
Potentially other, design-specific requirements

## Slide 3: Layout Steps
Define board shape.
Place mechanically important parts
Define power planes
Place other parts
Route the board
Run DRC

## Slide 4: Keeping Your Design Synchronized
It’s important to keep your .brd and .sch files synchronized.
If they get unsynchronized, it can be very hard to fix.
Unfortunately, Fusion360 makes this harder than it should be.

## Slide 5: The Three Files In Your Project
Schematic – your schematic
Board – your board
Project – the link between them
Always open the project file
  This will open the schematic and board together.
  It will keep them synchronized.
If you upload a new design, you must upload both .sch and .brd
Schematic
Board
Project

## Slide 6: If They Become Unsynchronized
Stop!
Run ERC.
It will show you the differences.
Save your work. Try to fix them.
If you can’t, post on piazza.

## Slide 7: Board Shape
Be creative!
Have a theme!
Place the motor symmetrically
Build rings for motor mounts

## Slide 8: Logos and Artwork
You can put whatever you want in tPlace
  Give your quadcopter personality!
You can also design in metal and solder mask
  Silkscreen -- white
  Metal -- gold
  Metal + solder mask – bright color
  Solder mask – darker color
  No metal, no mask – beige-ish
Checkout the quadcopter logo on the boards for the class

## Slide 9: q

## Slide 10: Placing the Motors
The motors need to be symmetrical about the roll and pitch axes.
This means they need to form a rectangle
With four motors 2 configurations are possible
  X
  +
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 11: Part Placement

## Slide 12: Device Placement: Style
Put all your components on a 0.5mm grid
  Except for critical areas like the antenna driver.
Reference designators can go on 0.5 or 0.1mm grid.
Orient all your parts the same way for easy assembly.
  If you want
  It makes it marginally easier to place parts
Leave space between components for easy assembly
  If you’ve followed the guidance on tKeepout, this will be automatic
Make it pretty!
tKeepout

## Slide 13: Placing the IMU
The IMU should be roughly at the board center of mass.
Placing it at the origin is a good choice
Then place the motors symmetrically around it.
The orientation of the IMU is important.
  It’s axes of measurement (see the data sheet) need to correspond to pitch, yaw, and roll for your quad.

## Slide 14: Placing the Antenna
The antenna should be on the edge of the board
No metal near by
It will determine the location of your microcontroller.
  You must follow the reference design to layout the antenna driver and MCU

## Slide 15: Power and Ground

## Slide 16: Motor Power: Resistance
Motors take a lot of current!
We want all the power to go to the motors
Copper is an imperfect conductor
  Voltage drop on power lines is non-trivial
  Resistance is a function of aspect ratio
  0.5 mΩ/square
So, make the power lines wide!
  Use a trace-width calculator
  https://www.4pcb.com/trace-width-calculator.html

## Slide 17: Power and Ground Planes
Power planes are large areas of metal for carrying power and ground
  Low-resistance
  Low-inductance
  High-capacitance
Ground planes help with decoupling
Designing them in complex circuits is a whole discipline

## Slide 18: In Your Quadcopter
GND planes on top and bottom
Internally
  One power one ground
  One pair for regulated, one pain for battery
Battery plane
  Pretty wide everywhere (low resistance)
  It should connect the battery and the motor drivers
  There should be long traces – mostly vias
Regulated plane
  Should cover the MCU and IMU and vreg
  MCU and IMU power should be vias
Top: GND
Route 2: BAT_GND and GND
Route 15: VBAT and 2V5
Bottom: GND

## Slide 19: Decoupling Caps
Decoupling caps in the data sheets must be near the devices they are for
  MCU
  IMU
  Voltage regulator
The two 47uF caps should be centrally located on their respective power/ground planes
  VBAT/BAT_GND
  3V/GND

## Slide 20: High Current Traces
VBAT
BAT_GND
Motor Drivers
  One trace in each motor driver (FB1)
  Current come in on big vias and wide traces from VBAT
  Traverses MOSFET, motor, and FB1
  Current leaves via big vias and wide traces to BAT_GND
  PWM1 is thin, because it’s low current
(The BAT_GND connections on the motor is mechanical only)

## Slide 21: Routing

## Slide 22: Differential Pairs
These carry high-speed signals
  USB
  HDMI
  PCIe
  The radio output from the MCU
Two wires running parallel to each other
  Similar electrical characteristics
  Subject to similar interference
  Reduced EMF interference
Name them with ’_N’ and ‘_P’ in Fusion

## Slide 23: The Antenna
Our antenna is a strip of copper.
It is ~1/4 the wavelength of the 2.4GHz radio signal
It should be smooth
  No sharp corners
  They cause reflections at high speed

## Slide 24: The Antenna Driver
Note the short symmetrical differential pair from the MCU to the balun
Note the smooth, strait, wide trace from the balun to the antenna
No creativity here. We don’t have the equipment or software to debug problems.

## Slide 25: The Three Ways to Route
Auto router
  Fully-automatic routing, subject to constraints that you can set.
  The Fusion auto router is not good enough to do it all for you.
“Follow me”
  Assisted manual routing. The router will enforce the constraints you set.
Fan out
  Create circuit stubs to connect devices to power/ground

## Slide 26: Auto Router
Mixed reputation
  It can’t do everything
  Sometimes it does a bad job
  When it works, it’s great.
  Usually, it needs some touch up.
Net classes (“Edit->Net Classes…”)
  Lets you set widths and clearances for different kinds of nets

## Slide 27: Semi-Automatic Routing
Route critical nets with follow me router
  Wires to antenna
  Wires to crystal
  Ground isolation for antenna and crystal
Fan out power and ground.
Autoroute everything else.

## Slide 28: Commands for Routing
“Auto;” – run the auto router (leave off the “;” to configure the router.
“Ripup” – unroute signals
“Show <thing>” – Highlight a net or part

## Slide 29: Design Rules Check
Checks that your board layout meets design requirements for manufacturing.
  Distance between traces and traces, traces and vias, etc.
  Trace width
  Etc.

## Slide 30: Electrical Rules Check
This checks for common problems in schematics.
Make sure you understand the reason for the errors.
Fix them if you can.
Run it!

## Slide 31: CAM Files

## Slide 32: CAM Layers (Gerber files)
Fusion layers are for design.
CAM layers are for manufacturing
  “Gerber” files are for lithographic steps
  Drill files are for drilling holes.
Each CAM layers corresponds to one layer of the resulting board
  Top silk screen (.PLC)
  Top solder mask (.STC)
  Top metal (.TOP)
  Inner metal layers
  Bottom metal (.BOT)
  Bottom solder mask (.STS)
  Bottom silk screen (.PLS)
  Different board houses have different suffixes.
One drill file specifying where all the pads, vias, and mounting holes are located and their diameters (.DRD)
Other files too, depending on the manufacturing process
  Solder paste stencil
  Assembly drawings

## Slide 33: The CAM Processor
The CAM Processor generates CAM files
The exact configuration for the gerber files varies by board house
  Should the board outline be in every layer?
  Which format should the files be in (there are many)
  Should the back side layers be mirrored?

## Slide 34: CAM Setup
To prepare Gerbers for a particular board house, you need CAM setup files (*.cam for Fusion)
This specifies how to generate each layer the board house needs.
See example in Button and Light Tutorial.

## Slide 35: Checking Your Gerbers!
Fusion can’t display Gerber files itself
You need a 3rd party tool
  See the Button and Light tutorial for recommendations
You should always check your Gerbers!
  Fusion has bugs (you should assume)
  You may have misconfigured something
  You may have put something in the wrong layer.

## Slide 36: Part Placement Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 37: Power Planes Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 38: Net Classes and Routing Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 39: Silkscreen Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 40: CAM File Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu