## Slide 1: Agenda
Questions about lab 2
Programming hardware lab overview
PCB assembly lab part 1:
  PCB assembly overview
  Assembly group 1 collects parts for their chargers.

## Slide 2: Programming The Hardware
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 3: Assembling Everything
Detailed instructions in the lab
And a fancy video

## Slide 4: Software Plan
This Lab
  Meet the hardware
  Learn to use it
Sensing Lab – IMU Filtering
PID Lab – Implement control
Flight Lab – Flight!
Do everything on the Test Stand first, then move to your quadcopter

## Slide 5: Take Care of the Equipment
The remote and FCB are loaned to you.
Take care of them!!!
If you break them through neglect or abuse or loose them, you must pay for their replacement/repair.

## Slide 6: Quadcopter Firmware
Basic operation
  Control motors
  Read IMU
Sensing
  Use the IMU to measure the orientation of the quadcopter
  Filter IMU readings to eliminate noise
Control
  Based on IMU measurements, maintain stability
  Receive commands from remote
  Implement them

## Slide 7: Remote Firmware
Control
  Measure gimbal position
  Transmit readings to the quadcopter
Tuning
  Your control algorithm will have many parameters
  You’ll need to tune them in real time
  Use the knob and buttons to make this easy
    or don’t… and suffer the consequences (extreme tedium and slow progress on tuning)

## Slide 8: This Lab
Use everything
  Install IMU library. Read values from IMU.
  Read the values from the gimbals.
  Drive the motors.
  Read values from the knob and buttons.
Build remote-controlled motors
  FCB drives motors.
  Remote control reads gimbals and transmits value to run motor at.
  This is the basic framework for your quadcopter and remote firmware.

## Slide 9: The Flight Control Board

## Slide 10: The Hardware You Will Build

## Slide 11: Brushed Motors
Speed ∝ Voltage ∝ Current
Vary the input voltage
Generating varying voltages is non-trivial.
  You need a digital-to-analog converter
Really, we just need the average voltage to vary

## Slide 12: Pulse Width Modulation
PWM varies the average voltage using a digital signal
  Duty cycle: % of time signal is high
  Cycle time: delay between rising edges (~2ms on our MCU – 490Hz)

## Slide 13: PWM in Arduino
The motors are connected to the FCB via analog output (PWM) pins
analogWrite (int pin, int v)
  ‘v’ is the duty cycle (0…255)
  ‘pin’ is the the pin

## Slide 14: The IMU

## Slide 15: 9-axis IMU
3-Axis accelerometer
  Gravity + trigonometry = pitch and roll
3-Axis gyroscope
  Directly measures rate of change for pitch, roll, and yaw
3-Axis magnetometer (compass)
  Could measure yaw, in theory.
  Calibration is hard, in practice.
  We won’t use this.

## Slide 16: 6-axis IMU
3-Axis accelerometer
  Gravity + trigonometry = pitch and roll
3-Axis gyroscope
  Directly measures rate of change for pitch, roll, and yaw

## Slide 17: IMU In Arduino
There’s a nice library for our IMU
  It does the trigonometry for you
  Provides convenient functions for reading all the values
Forked from Adafruit
  Thanks, Limor Fried!
A lot more detail in the next lab

## Slide 18: Powering the Quad
The FCB is powered by its battery.
  It must be installed to program it.
The FCB runs through batteries quickly
  You can tell the battery is low when it starts resetting when you turn on the motors

## Slide 19: The Remote

## Slide 20: The Remote PCB
Microcontroller + radio
  Identical to FCB
UI Controls
  Mostly for tuning PID
Gimbal connectors
USB-Serial Arduino Programmer
  For remote and FCB
Battery Charger
LCD

## Slide 21: Gimbals
Gimbal: a mechanism, typically consisting of rings pivoted at right angles
Standard aircraft controls
  Left: throttle and yaw
  Right: pitch and roll
Yaw, pitch, and roll are spring-loaded to return to neutral
Throttle stays where you put it.

## Slide 22: Anatomy of a Gimbal
Two potentiometers measure X and Y movement of the stick.
Potentiometer – A variable voltage divider
  As the slider’s movement changes the resistance from A and W and W and B.
  The voltage at W is proportional to the position of the gimbal.
The resistances are always > 0, so VW never reaches VA or VB.
Older gimbals:
  Frsky PR10 – common in quad remotes
  Total resistance: 2.4KOhms
  Rated voltage: 5V
Newer gimbals
  Hall effect sensors
  They are “pin compatible” with the older gimbals
VA = 0
VB = 3.3V
VA-W + VW-B = VB-VA
AnalogRead() = VW/VB * 1024

## Slide 23: Reading the Gimbals
The gimbals are connected to analog input pins on the MCU
analogRead(int pin)
  Takes a voltage between GND and Vcc and maps it to 0—1024
The Remote library defines constants for which pins to read.
  firmware/libraries/Remote/quad_remote.h

## Slide 24: Status LEDs
The remote has 2 status LEDs
They are useful for letting you know when the quad is armed, etc.
Use digital_write() to control them.
See quad_remote.h for pins

## Slide 25: Buttons
The remote has 7 buttons.
  1 ”D-pad” – up, down, left, right, center
  2 others (btn1, btn2)
The Remote library has two interfaces
  Call-backs: A function that is called when a button is pressed.
  is_pressed(): Check if a button is currently pressed.
Potential problems
  Sometimes one press appears as several due to “bouncing”

## Slide 26: Rotary Encoder
The knob is ‘rotary encoder’
It can turn indefinitely in either direction.
The Remote library tracks its movement
  Query current value with: knob1.getCurrentPos ()
  Set current value with: knob1.setCurrentPos()
The knob also has a built-in button. It works just like the others.

## Slide 27: Battery Chargers
Remote’s integrated battery charger
  Powered via USB
  It draws less than 500mA, which is the USB standard
Duo LiPo charger
  Usually, we assemble this in class
  Needs a higher-powered USB port (like a tablet charger)
  ~1A max (with two batteries constant-current charging)
  It gets a little hot
Status lights
  Green means charged
  Red means charging
  Both mean no battery
The FCB/Quad runs through batteries fast
  Keep chargers occupied

## Slide 28: Arduino Programmer
A USB-serial converter connects to your laptop
The switch at lower-right routes the serial line
  Remote control MCU (“RC”)
  4-pin programming port (“QUAD”)
  Match ‘B’ to black wire and ‘G’ to green wire.
The remote programs itself and the quadcopter via USB
Serial debugging with Arduino

## Slide 29: LCD
The LCD can provide feedback to the pilot.
  UI for calibration and tuning
The Remote library defines an object called `lcd`
  You write to it just like a serial port.
  Some other operations too.
  See lab and examples.
It has a RGB backlight 

## Slide 30: The Radio

## Slide 31: Standard and Software Interface
The remote, FCB, and your quadcopter use the same radio.
  2.4GHz IEEE 802.15.4
  Physical and media access control (MAC) layers
  Common basis for embedded wireless standard (e.g., Zigbee, 6LoWPAN)
The ‘Radio.h’ library provides access.
There are 11 channels
  Eaglint will allocate your team a channel when you create your group.
  It’s not private, so you must share nicely – don’t transmit constantly
  Set your channel with: rfBegin(WIRELESS_CHANNEL);
Send data with: rfWrite(<data>)
Receive data (if available) with : rfRead(<data>)

## Slide 32: Radio: What To Send
You must define the packet format for your remote/quad.
  The easiest thing to do is define a struct that has everything you need.
  It can be up to 128 bytes
You must reject packets from other sources (noise and other teams)
  Include a ‘magic number’, unique to your team
  Include a checksum (highly recommended)
  Always check the length of the data you read (it should match the size of your struct)
You will need to send telemetry from the quad too
  At least to managing arming properly.
  And whatever else you want.
  You can (and probably should) use a different packet format.

## Slide 33: For Next time:
Add a slide about sparsing the stream of bytes and how to get re-aligned if you miss something.

## Slide 34: Remote Controlled Motors

## Slide 35: The Basics for Your Remote and Quad Firmware
Remote
  Read user input
  Build a simple user interface
  Transmit commands to the quadcopter
  Calibration
  Arming (for safety)
Quadcopter
  Receive commands
  Control the motors
  Arming (for safety)

## Slide 36: Remote Software Path
Scale and bound gimbal readings
  P, Y, R: -128 to 127
  T: 0 to 255
Tuning parameters
  Set tuning parameters with the UI
  Send them to the quadcopter
Transmit updates at 10-20Hz.
  No faster – share the spectrum!

## Slide 37: Quadcopter Datapath for This Lab
Read the throttle
Control the motors
Separately: Verify you can read the IMU

## Slide 38: Arming the Quad
Your motors should not turn on accidently (e.g., by default, if the throttle happens to be on, if you bump the throttle) – it’s dangerous
Your firmware must properly ”arm” the quadcopter
  Push the gimbals out and down (left to lower left, right to lower right)
  Forces throttle to zero.
  Unlikely to happen by accident.
Turn on an LED on the FCB when it is armed.
Turn off the LED when it’s disarmed.
Resetting the remote or the FCB should disarm both.

## Slide 39: Calibration
The actual range of values from your gimbals will vary.
You need a consistent range to control your quad.
Your remote needs a calibration mode where it learns the actual range
You should map the actual range to (0-255) for throttle, and (-128 to 127) for everything else
Requirements
  Calibration mode should only be available when the FCB is disarmed
  You must save the calibration measurements in the MCU’s EEPROM (see lab for details)
  You must provide some feed back via the LCD so the user knows what’s going on.

## Slide 40: Programming the FCB and the Remote with the Arduino IDE
User-friendly IDE for Arduino programming
  Programming the microcontroller is easy
  Installation is easy
  Use version >= 1.8.12
Settings
  Tools->Board->Quad Class Atmega…
  Tools->programmer->USBTinyISP
  Tools->Port->Com n (windows, choose largest n available)
  Tools->Port->cu… (pick the one that appeared when you plugged in the remote)

## Slide 41: Demo
Walk through knobs_and_buttons.ino
Demo solution

## Slide 42: Form groups
This lab (and all future) are in (the same) groups of two.
Create group on eaglint
Create group assignment on github classroom
  Use exactly the same name!

## Slide 43: Assemble the Remote and Test Stand
Come up and get a kit.
Get started.
Instructions are and photos are in the lab.
There’s a video online.

## Slide 44: The End

## Slide 45: Assembling the Quadcopter and Remote
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 46: Programming The Hardware Lab Checklist Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 47: Changing the Polarity of Your Motors
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 48: Next Time
30 minutes of questions
70 minutes of lecture
They completed assembly of the remotes and test stands in 1-2 hours.

## Slide 49: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 50: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 51: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 52: Demos
Show PWM signal changing duty cycle
Show flyback
  Effect of diode
  Show effect on power supply noise
Show filter on pwm line
  Effect of resistor and capacitor on PWM
  Show output of FET
  Show affect of filter on power supply noise