## Slide 1: Programming The Hardware
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 2: Take Care of the Equipment
The remote and FCB are loaned to you.
Take care of them!!!
If you break them through neglect or abuse or loose them, you must pay for their replacement/repair.
If you want to build your own remote, talk to me.

## Slide 3: The Hardware You will Build

## Slide 4: The Hardware You Will Build

## Slide 5: Controller
Read user input for flight
  2 ”gimbals”
    Left: throttle and yaw
    Right: pitch and roll
  Yaw, pitch, and roll are spring-loaded to return to neutral
  Throttle stays where you put it.
Buttons and a knob for tuning
A radio for communication
A battery charger

## Slide 6: Programming the Remote and FCB
The remote has a built-in USB-serial converter that works with Arduino.
It has two modes
  RC mode – programs the remote
  Quad mode – Sends programming signals via header.
To program FCB
  Connect FCB to remote with 4-strand cable
  Match ‘B’ to black wire and ‘G’ to green wire.

## Slide 7: Powering the FCB
The FCB is powered by its battery.
There’s no power switch. Unplug the battery.
The FCB runs through batteries quickly
  Keep your remote plugged in and charging.
  Keep your battery charger charging.
  Swap when FCB battery get low (i.e., it starts resetting when you turn on the motors)

## Slide 8: The Arduino IDE
User-friendly IDE for Arduino programming
  Programming the microcontroller is easy
  Installation is easy
Settings
  Tools->Board->Quad Class Atmega…
  Tools->programmer->USBTinyISP
  Tools->Port->Com n (windows, choose largest n available)
  Tools->Port->cu… (pick the one that appeared when you plugged in the remote)

## Slide 9: Software Plan
This Lab
  Meet the hardware
  Learn to use it
Sensing Lab -- IMU Filtering
PID Lab -- Implement control
Do everything on the Test Stand first, then move to your quadcopter

## Slide 10: Quadcopter Firmware
Sensing
  Use the IMU to measure the orientation of the quadcopter
  Filter IMU readings to eliminate noise
Control
  Based on IMU measurements, maintain stability
  Receive commands from remote
  Implement them

## Slide 11: Remote Firmware
Control
  Measure gimbal position
  Transmit readings to the quadcopter
Tuning
  Your control algorithm will have many parameters
  You’ll need to tune them in real time
  Use the knob and buttons to make this easy
    or don’t… and suffer the consequences (extreme tedium and slow progress on tuning)

## Slide 12: Lab Tasks
Use everything
  Install IMU library. Read values from IMU.
  Read the values from the gimbals.
  Drive the motors.
  Read values from the knob and buttons.
Build remote-controlled motors
  FCB drives motors.
  Remote control reads gimbals and transmits value to run motor at.
  This is the basic framework for your quadcopter and remote firmware.

## Slide 13: The Hardware

## Slide 14: Brushed Motors

## Slide 15: Construction

## Slide 16: Operation

## Slide 17: Operation

## Slide 18: Operation

## Slide 19: Operation

## Slide 20: Operation

## Slide 21: Controlling Brushed Motors
Speed ∝ Voltage ∝ Current
Vary the input voltage
Generating varying voltages is non-trivial.
  You need a digital-to-analog converter
Really, we just need the average voltage to vary

## Slide 22: Pulse Width Modulation
PWM varies the average voltage using a digital signal
  Duty cycle: % of time signal is high
  Cycle time: delay between rising edges (~2ms on our MCU – 490Hz)

## Slide 23: PWM in Arduino
The motors are connected to the FCB via analog output (PWM) pins
analogWrite (int pin, int v)
  ‘v’ is the duty cycle (0…255)
  ‘pin’ is the the pin

## Slide 24: Gimbals

## Slide 25: The Gimbals
Each stick is a “gimbal”
  a mechanism, typically consisting of rings pivoted at right angles

## Slide 26: Anatomy of a Gimbal
Two potentiometers measure X and Y movement of the stick.
Potentiometer – A variable voltage divider
  As the slider’s movement changes the resistance from A and W and W and B.
  The voltage at W is proportional to the position of the gimbal.
In reality, the resistances are always > 0, so W never reaches VCC or GND.
Our gimbal
  Frsky PR10
  Total resistance: 2.4KOhms
  Rated voltage: 5V

## Slide 27: Reading the Gimbals
The gimbals are connected to analog input pins on the MCU
analogRead(int pin)
  Takes a voltage between GND and Vcc and maps it to 0—1024
The Remote library defines constants for which pins to read.
  firmware/libraries/Remote/quad_remote.h

## Slide 28: Status LEDs
The remote has 2 status LEDs
They are useful for letting you know when the quad is armed, etc.
Use digital_write() to control them.
See quad_remote.h for pins

## Slide 29: Buttons
The remote has 7 buttons.
  1 ”D-pad” – up, down, left, right, center
  2 others (btn1, btn2)
The Remote library has two interfaces
  Call-backs: A function that is called when a button is pressed.
  is_pressed(): Check if a button is currently pressed.
Potential problems
  Sometimes one press appears as several due to “bouncing”

## Slide 30: Rotary Encoder
The knob is ‘rotary encoder’
It can turn indefinitely in either direction.
The Remote library tracks its movement
  Query current value with: knob1.getCurrentPos ()
  Set current value with: knob1.setCurrentPos()
The knob also has a built-in button. It works just like the others.

## Slide 31: Radio
The remote and FCB (and your quadcopter) all use the same radio.
The ‘Radio’ library provides access.
There are 11 channels
  Eaglint will allocate your team a channel when you create your group.
  Since you are at home, the channel doesn’t matter that much. You can use whatever you like. Some will be noisier around your house than others.
  It’s not private, so you must share nicely – don’t transmit constantly
  Set your channel with: rfBegin(WIRELESS_CHANNEL);
Send data with: rfWrite(<data>)
Receive data (if available) with : rfRead(<data>)

## Slide 32: Radio: What To Send
You must define the packet format for your remote/quad.
  The easiest thing to do is define a struct that has everything you need.
  It can be up to 128 bytes (I think)
You must send the data you need
You must reject packets from other sources (noise and other teams)
  Include a ‘magic number’, unique to your team
  Include a checksum (highly recommended)
  Always check the length of the data you read (it should match the size of your struct)

## Slide 33: Remote Software Path
Scale and bound gimbal readings
  P, Y, R: -128 to 127
  T: 0 to 255
Tuning parameters
  Set tuning parameters with the UI
  Send them to the quadcopter
Transmit updates at 10-20Hz.
  No faster – share the spectrum!

## Slide 34: Quadcopter Datapath for This Lab
Read the throttle
Control the motors

## Slide 35: LCD
The LCD can provide feedback to the pilot.
  UI for calibration and tuning
The Remote library defines an object called `lcd`
  You write to it just like a serial port.
  Some other operations too.
  See lab and examples.
It has a RGB backlight 

## Slide 36: Remote Controlled Motors

## Slide 37: Arming the Quad
Your motors should not turn on accidently (e.g., by default, if the throttle happens to be on, if you bump the throttle) – it’s dangerous
You firmware must support ”arming” the quadcopter
  Push the gimbals out and down (left to lower left, right to lower right)
  Forces throttle to zero.
  Unlikely to happen by accident.
Turn on an LED on the FCB when it is armed.
Turn off the LED when it’s disarmed.
Resetting the remote or the FCB should disarm both.

## Slide 38: Calibration
The actual range of values from your gimbals will vary.
You need a consistent range to control your quad.
Your remote needs a calibration mode where it learns the actual range
You should map the actual range to (0-255) for throttle, and (-128 to 127) for everything else
Requirements
  Calibration mode should only be available when the FCB is disarmed
  You must save the calibration measurements in the MCU’s EEPROM (see lab for details)
  You must provide some feed back via the LCD so the user knows what’s going on.

## Slide 39: Demo
Walk through knobs_and_buttons.ino
Demo solution

## Slide 40: Form groups
This lab (and all future) are in (the same) groups of two.
Create group on eaglint
Create group assignment on github classroom
  Use exactly the same name!

## Slide 41: Assemble the Remote and Test Stand
Come up and get a kit.
Get started.
Instructions are and photos are in the lab.
There’s a video online.

## Slide 42: The End

## Slide 43: Assembling the Quadcopter and Remote
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 44: Programming The Hardware Lab Checklist Demo
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 45: Next Time
30 minutes of questions
70 minutes of lecture
They completed assembly of the remotes and test stands in 1-2 hours.

## Slide 46: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 47: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 48: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 49: Demos
Show PWM signal changing duty cycle
Show flyback
  Effect of diode
  Show effect on power supply noise
Show filter on pwm line
  Effect of resistor and capacitor on PWM
  Show output of FET
  Show affect of filter on power supply noise