## Slide 1: Programming The Hardware

## Slide 2: The Flight Control Board

## Slide 3: Controller
Read user input for flight
  2 ”gimbals”
    Left: throttle and yaw
    Right: pitch and roll
  Yaw, pitch, and roll are spring-loaded to return to neutral
  Throttle stays where you put it.
Buttons and a knob for tuning
A radio for communication
A battery charger

## Slide 4: The Test Stand

## Slide 5: The Arduino IDE
User-friendly IDE for Arduino programming
  Programming the microcontroller is easy
  Installation is easy

## Slide 6: Software Plan
This Lab
  Meet the hardware
  Learn to use it
Sensing Lab -- IMU Filtering
PID Lab -- Implement control
Do everything on the Test Stand first, then move to your quadcopter

## Slide 7: Quadcopter Firmware
Sensing
  Use the IMU to measure the orientation of the quadcopter
  Filter IMU readings to eliminate noise
Control
  Based on IMU measurements, maintain stability
  Receive commands from remote
  Implement them

## Slide 8: Remote Firmware
Control
  Measure gimbal position
  Transmit readings to the quadcopter
Tuning
  Your control algorithm will have many parameters
  You’ll need to tune them in real time

## Slide 9: Lab Tasks
Use everything
  Install IMU library. Read values from IMU.
  Read the values from the gimbals.
  Drive a motor.
  Read values from the knob and buttons.
Build a remote-controlled motor
  FCB drives motors.
  Remote control reads gimbals and transmits value to run motor at.
  This is the basic framework for your quadcopter and remote firmware.

## Slide 10: Brushed DC Motors

## Slide 11: Brushed Motors

## Slide 12: Construction

## Slide 13: Operation

## Slide 14: Operation

## Slide 15: Operation

## Slide 16: Operation

## Slide 17: Operation

## Slide 18: Controling Brushed Motors
Speed ∝ Voltage ∝ Current
Vary the input voltage
Generating varying voltages is non-trivial
  You need an digital-to-analog converter
Really, we just need the average voltage to vary

## Slide 19: Pulse-width Modulation (PWM)

## Slide 20: PWM in Arduino
The red board board has several analog output (PWM) pins
analogWrite (int pin, int v)
  ‘v’ is the duty cycle (0…255)
  ‘pin’ is the the pin

## Slide 21: Gimbals

## Slide 22: The Gimbals
Each stick is a “gimbal”
  a mechanism, typically consisting of rings pivoted at right angles

## Slide 23: Anatomy of a Gimbal
Two potentiometers measure X and Y movement of the stick.
Potentiometer – A variable voltage divider
  As the slider’s movement changes the resistance from A and W and W and B.
  The voltage at W is proportional to the position of the gimbal.
In reality, the resistances are always > 0, so W never reaches VCC or GND.
Our gimbal
  Frsky PR10
  Total resistance: 2.4KOhms
  Rated voltage: 5V

## Slide 24: Reading the Gimbals
The red board board has several analog input pins
analogRead(int pin)
  Takes a voltage between GND and Vcc and maps it to 0—1024
The Remote library defines constants for which pins to read.

## Slide 25: Status LEDs
The remote has 2 status LEDs
They are useful for letting you know when the quad is armed, etc.
Use digital_write() to control them.
See Remote.h for pins

## Slide 26: Buttons

## Slide 27: Rotary Encoder

## Slide 28: Radio

## Slide 29: Remote Software Path
Scale and bound gimbal readings
  P, Y, R: -512-512
  T: 0-1023 for T
Tuning parameters
  Set tuning parameters with the UI
  Send them to the quadcopter
Transmit updates at 10-20Hz.
  No faster – share the spectrum!

## Slide 30: Quadcopter Datapath
Read the throttle
Control the motors

## Slide 31: The End

## Slide 32: Principles of Operation (1)
Z
Y
X
An even number of motors provides lift and control in 6 dimensions
  Spatial dimensions: x, y, z
  Pitch: rotation around left-right (y) axis
  Roll: rotation around the front-back (x) axis
  Yaw: rotation around the top-bottom (z) axis
A flight computer operates a closed-loop controller to maintain stability and implement pilot commands.

## Slide 33: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 34: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 35: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 36: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 37: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 38: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 39: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 40: Lab 3: Make all Your Hardware Work a.k.a Remote Controlled Motors

## Slide 41: Demos
Show PWM signal changing duty cycle
Show flyback
  Effect of diode
  Show effect on power supply noise
Show filter on pwm line
  Effect of resistor and capacitor on PWM
  Show output of FET
  Show affect of filter on power supply noise

## Slide 42: The Inputs and Outputs
Gimbals – How they work and how to read them.
Brushed Motors – How they work and how to drive them.
The IMU – microcontroller and IMU communicate.
The serial display, LEDs, etc. – Communicating with the pilot.

## Slide 43: Flyback
Opening S1 makes M1 an inductor
  Drives up voltage M1-
  Can destroy the switch
  Can cause current to back to power supply.
  Causes noise on power supply.
This is called “fly back”
Adding a diode relieves the problem.

## Slide 44: Motor Driver
Pulse-width modulation (PWM)-controlled MOSFET
  The microcontroller will drive the MOSFET
  The MOSFET will drive current to the motor.

## Slide 45: Our Motor Circuits

## Slide 46: The Serial LCD Display

## Slide 47: Display Text on the Remote
The LCD display on the remote is connected to the second serial port on the redboard
The LCD_library provides a nice interface for writing to it
  Docs here: http://playground.arduino.cc/Code/SerLCD