## Slide 1: Sensing and Filtering Quadcopter Orientation
Dr. Steven Swanson
CSE176e/276e
swanson@cs.ucsd.edu

## Slide 2: Basic Flight Algorithm
Receive target orientation (Done!)
Sense quad orientation (This Lab)
Adjust motor output to correct orientation (Next two labs)
Goto 1 (Done!)

## Slide 3: Lab Tasks
Read values from IMU.
Use Arduino’s plotting tool
Run your serial port at max speed!!!
Read the pitch of your test stand with the motors on
  Configure the filters on the IMU
  Implement a complimentary filter in software.
  Make it work in the presence of motor vibrations.

## Slide 4: Pitch, Yaw, and Roll Angles
3 angles to specify an orientation
The AHRS library gives you the pitch and roll angles
We are only using ‘pitch’ in this lab.

## Slide 5: Brief (and Incomplete) Explanation of High- and Low-Pass Filters

## Slide 6: Signal and Signal Domains
Signals are just time-varying values (e.g., a pitch or roll angle)
Time domain
  x-axis is time
  y-axis is amplitude
Frequency domain
  x-axis is frequency
  y-axis is intensity
“High-Frequency” == Rapidly changing
”Low-Frequency” == slowly changing
Time Domain
Frequency Domain

## Slide 7: Signals Filters
Filters attenuate some frequencies in a signal
  Low-pass filter attenuate high-frequencies
  High-pass filters attenuate low-frequencies
Ex.: A low-pass filter can eliminate high-frequency noise

## Slide 8: Accelerometer
Measure forces acting on the quadcopter along 3 axes
  You can measure gravity’s direction using the the three axes.
  Some trigonometry will yield Euler angles
Strengths
  No drift
  Good low-frequency performance
Weaknesses
  Susceptible to vibration
  Any acceleration (e.g., movement) will add error.
  Poor high-frequency performance

## Slide 9: Gyroscope
Directly measures rate of change for pitch, roll, and yaw
Integrating will give you those angles (given a starting point)
  “dead reckoning”
Strengths
  Less susceptible to noise
  Good high-frequency performance
Weaknesses
  The integral will drift
  Poor low-frequency performance

## Slide 10: Complimentary Filter
Combine the best of accelerometer and gyro
  High-frequency from the gyroscope
  Low frequency from the accelerometer
The math is pretty simple
    θnew the new estimated Euler angle
    θold the previous estimated Euler angle
    dθg/dt gyro measurement
    Δt Time since last gyro measurement
    θa Angle from the accelerometer
    C The “complimentary gain”
See the video for details
θnew = C*(θold + Δt*dθg/dt ) + (1-C)*θa

## Slide 11: Communicating With the IMU

## Slide 12: Reading and Writing “Registers”
I2C devices (and all modern, digital hardware devices) expose a set of “registers”
  Each register has an address
  Some are read-only
  Some are read-write
  Some are write-only
We read and configure the IMU by reading and writing to registers

## Slide 13: Reading And Writing Registers with I2C
Each I2C device has an “I2C address”
  8-bits
  You configured one of these bits in your schematic
Arduino provides the Wire library for I2C communication
  A little complicated – multi-byte access etc.
  We won’t use this directly
QuadClass-LSM6DSO provides some convenience functions
  void read8(boolean type, byte register_address)
  void write8(boolean type, byte register_address, byte value)
  Look at the library source code for details, if interested

## Slide 14: Sensing and Filtering in Our IMU

## Slide 15: Our IMU: LSM9DS1
Our IMU is two I2C devices in one package
  An Accelerometer+Gyroscope
    “XL” and “Gyro” in the datasheet
  A magnetometer
    We aren’t using this.

## Slide 16: Our IMU: LSM9DS1
An Accelerometer + Gyroscope
  “XL” and “Gyro” in the datasheet
Both have a complex set of filters we can use.
ODR == Output Data Rate
  How frequently you can read a new values from IMU

## Slide 17: Gyroscope Datapath

## Slide 18: Gyroscope Datapath

## Slide 19: Gyroscope Filtering API
The QuadClass_LSM6DSOX object you used in the first hardware lab has methods to configure the gyro filters
Documented in
  firmware/libraries/QuadClass-LSM6DSOX/QuadClass_LSM6DSOX.h
  firmware/libraries/Adafruit_LSM6DS/Adafruit_LSM6DS.h
 Controls LPF2
 Controls LPF1
 Controls HPF

## Slide 20: Example: setGyroLPF1()
QuadClass_LSM6DSOX.h
ODR (set by setGyroDataRate())
Low pass cut off frequency
filter_range parameter

## Slide 21: LSM9dS1 Key Points
ODR – Output Data rate
  How many readings per second does it the IMU take?
  There are two ways to set it
    One for just XL
    Another if both XL and G are active
Key Sections
  7.12, 7.13, 7.14, 7.24, 7.25
Reading data sheets is hard
  You must read carefully, and thoughtfully.
  It’s a bit of a puzzle.
  This is part of what you’re learning in this class

## Slide 22: Example: IMU Datasheet Section 7.12
firmware/libraries/QuadClass-LSM9DS1/Adafruit_LSM9DS1.h
firmware/libraries/QuadClass-LSM9DS1/Adafruit_LSM9DS1.cpp

## Slide 23
…
…

## Slide 24: Accelerometer Filters

## Slide 25: Accelerometer Filtering API
Methods
Documented in the same files
 Controls LPF1
 Controls LPF2 or HP Filter

## Slide 26: Example: setGyroLPF1()
QuadClass_LSM6DSOX.h
ODR (set by setAccelDataRate())
Low pass cut off frequency
filter_range parameter

## Slide 27: IMU Internal Accelerometer Filter

## Slide 29: Filter Demo

## Slide 30: Tuning
Two goals
  Low noise
  Low lag

## Slide 31: Gyro Clipping
Clipping occurs when the measured value exceed what the IMU can measure
Since we are integrating the gyroscope, clipping is especially bad.
Fix it by setting the resolution of your gyroscope.

## Slide 32
Gyro values are scaled down so the fit more nicely on the y axis.

## Slide 33
Gyro values are scaled down so the fit more nicely on the y axis.

## Slide 34
Gyro values are scaled down so the fit more nicely on the y axis.

## Slide 35: Quadcopter Datapath
Use complimentary filter to blend acc. And gyro data
  Pitch and roll
  Complimentary gain should come from the remotse

## Slide 36: The End

## Slide 37: Next time
More details and updated code about writing to registers
More detailed discussion of XL datapath and filtering.
Slides about LP and HP filters.
These slides + assembly slides took about 60 min.
30 min of questions at the start.
Adjust complimentary filter demo, so it’s easier to get to C = 0

## Slide 38: The PID Controller

## Slide 39: To add
Discuss different ways they can control their quad
  Pitch/roll -> rate of change of angle
  Pitch/roll -> angle of attack
  Pitch/roll -> velocity
  Pitch/roll -> position
  Throttle -> throttle
  Throttle -> rate of climb
  Throttle -> altitude
Discuss higher-order control
  How to integrate GPS
  How to integrate barometer

## Slide 40: Note for Next Class
Demo
  Integral windup
  Tuning PID
Combine this lecture with the flight control software lecture

## Slide 41: Control Theory
Making a physical system do what you want
“Open loop” and “closed loop”
Open loop - cannot see the system’s output
  Motor controllers
  LCD/LED/CRT screens
Closed loop - Can see output, make corrections
  Autopilot
  GPS guided munitions
  Our quadcopter

## Slide 42: What is PID?
Make a system follow a set point
“Proportional, Integral, Derivative”
A brief history:
  1788 - James Watt’s flyball governor (P)
  1837 - Louis Molinié hydraulic regulator (PI)
  1857 - H.N. Throop marine engine governor (PD)
  1868 - Maxwell gives theoretical basis
  1911 - Elmer Sperry, ship steering (PID)

## Slide 43: Closed loop control
PID is the most common closed loop controller
Proportional: Directly against error
Integral: Remembers error over time
Derivative: Dampens response to avoid oscillations

## Slide 44: Example
https://sites.google.com/site/fpgaandco/pid

## Slide 45: PID on the Quadcopter
3 separate controllers
PID set point is from user

## Slide 46: Pitfalls of PID
Integral term “Windup”
  One solution: Exponential decay on integral (E.g., I = I/2 + error)
Derivative noise: beware of noise.
Error term with vibration
Derivative term causes your system to go insane
  Solution: moving average of last several values. Or median of last several values.
  Using the serial plotter in arduino to watch the D term.
3. Tweaking PID values
Tune P first, then D, then I.

## Slide 47: Implementation
NOTES:
  Where to get the derivative?
  Integral windup
  Pay attention to rate (hz)
  Relative scale of inputs and outputs
    Make sure timestep is consistent

## Slide 48: How important in speed?
The key number is how many times/sec your PID loops (Hz)
The internet suggests > 100Hz (10ms/cycle) is necessary for stable flight.
My non-optimized code runs at 400Hz (2.5ms/cycles)
Action | Latency (ms)
Reading IMU | 7.360
analogWrite() | 0.012
analogRead() | 0.104
Integer PID (one channel) | 1.880 (531Hz)
FP PID (one channel) | 1.888 (529Hz)
AHRS getOrientation() | 1.860
rfWrite() 16 bytes | 0.812
Serial.write(“a”) | 0.906

## Slide 49: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 50: Tuning
Tuning PID is a bit of an art form.
Simple algorithm
  Set P=I=D = 0
  Increase P until it starts oscillating, reduce until it oscillates just a bit
  Increase D to till it stabilizes pretty quickly
  Increase I to fix offset
  Increase D as much as possible with causing oscillation.

## Slide 51: Tuning
Zeigler-Nichols method.
  P=I=D= 0
  Increase P until oscillations start. P is now at Ku, oscillation is at frequency Tu.
  Follow the chart.
  It’s important that your PID look incorporate its execution interval correctly.

## Slide 52: Slides on Sensors
Accelerometer
  Demo the data we get (3-axis accelerations)
  Conversion to Euler angles. Show math.
  Conversion to acceleration along x,y,z?
  Maybe talk about coordinate systems?
Gyroscope
  Demo the data we get
Other sensors
  GPS
  Barometer
  Magnetometer
  Temperature (for correcting measurements)
    https://wiki.dronecode.org/_media/u01.imu_temperature_compensation_-_hessel_van_der_molen.pdf

## Slide 53: New Slides on Filters
Noise
Calibration
Demo of noisy measurements
Demo of progressive improvements
  Calibration
  Tuning filters in the quadcopter
  Tuning complimentary filter
    Demo Drift from integrating gyroscope
  Tuning moving average on euler angles
Demo of “good” pitch/roll angle measurements
Discuss magnetometer?
  Calibration: https://github.com/kriswiner/MPU-6050/wiki/Simple-and-Effective-Magnetometer-Calibration
  Heading calculations

## Slide 54: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 55: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 56: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 57: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 58: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6